## Slide 1: Ground School and Flight Training Marymoor R/C Club, Redmond, WA AMA Charter 1610
Page 1
Version 1.8 – Sept 28, 2017

## Slide 2: Version Information
Version | Author | Date | Description
.5 | Eric | 3/27/2015 | First Draft
.6 | Brian | 15-Apr | Second Draft
1 | Eric, John and Brian | 5/4/2015 | First Version for release
1.1 | Eric | 5/4/2015 | Comments from Steve Guty, Doug, Ian
1.2 | Eric | 5/10/2015 | Edits for sections
1.3 | Brian | 5/24/2015 | Misc. Edits, photos, and added content
1.4 | Brian Kelly | 5/3/2016 | FAA registration, recommend electric. Edits and sequence for clarification
1.5 | Brian Kelly | April 2017 | Aligned Flight Training Syllabus with new flight log. Misc corrections and refinements
1.6 | Brian Kelly | 4/19/2017 | Misc edits, repaired links, to prepare for website update
1.7 | Brian Kelly | 4/26/2017 | Corrections and misc edits
1.8 | Brian Kelly | 9/28/2017 | Updated Proficiency Check and misc edits
Copyright © 2017 Marymoor Radio Control Club mar-c.org
Page 2

## Slide 3: A safe, inspiring, and educational training experience
Any Time of year: Come to the field and ask around for someone to teach you to fly
Summer Training Program:
    FREE – Run by club volunteers
    Your first lesson on the club trainer
    After this, you must provide your own airplane and transmitter, and apply for memberships (free if 18 or under, see following slides)
    Tuesdays 5 PM to sunset (weather permitting), from approximately first week in May through last week in August.
    For new student pilots or for returning pilots that need to brush up on their flying skills
    Minimum age depends on aptitude and motivation of the individual student – usually at least 10 years old.
Instructor and student each hold a transmitter, and the two are connected by a “buddy box” connector cord so the instructor can always assure safe flying
        BEFORE YOUR BUY ANYTHING, READ SECTION 2, Selecting your training airplane and radio
Page 3
Notes: Our goal is for all students to enjoy a safe and inspiring training experience. In the links we provide information that can be a bit intimidating at first. Rest assured that we are enthused about helping you, as we have done for many, many new fliers. After all, flying is a lot more fun when we have new friends to share it with!
AMA membership (http://www.modelaircraft.org) and MAR/C membership are required. Until the student passes a test, the membership will be “provisional”.
MAR/C conducts a flight training program each year for new student pilots or for returning pilots that need to brush up on their flying skills:
  Tuesdays 5 PM to sunset (weather permitting), May 5th through August 26th.
  A new pilot may fly a MAR/C owned trainer with an instructor for one flight prior to joining the training program.
  During summer training nights, MAR/C will provide a “buddy box” and cord to connect the student and instructor’s transmitters:
The club currently supports Spektrum and Futaba brands.
If the student owns a transmitter of some other brand, they must invest in their own buddy box (e.g. a second transmitter) of the same brand, and the connecting cord.
Both the primary transmitter and the “buddy box” transmitter must be of a similar vintage and be able to use the same type of cord and connections.
  Direct any questions that you may have to Flight Training Manager Steve Lenz (425-391-0657 or Mike Powell (425-883-2465).
Alternatively you could arrange privately with a willing club member to teach you to fly at any time of the year. When the student is ready to graduate from “provisional” to “full” membership, the student must pass a flight exam with a club board member, in the same manner as the training program.
Before purchasing your own airplane and other equipment, please read Selecting An Airplane and contact one of the above MAR/C contacts if you have any questions. Also, please come visit the field and talk to other pilots, to see the equipment in use and get a feel or the size and capabilities of different kinds of trainers. If possible, the Tuesday training evenings are the best opportunity for this. Deciding what to buy based only on website and advertisement information usually results in disappointment.

## Slide 4: Disclaimers
MAR/C provides advice. After you gain solo flight privileges, only you are responsible for your model aircraft readiness, your actions, and abilities
Any instructions provided by the manufacturers of
equipment such as but not limited to aircraft, radio controls, batteries, motors or engines
and anything installed in your airplane have
precedence over any advice provided by instructors, this document, or the mar-c website..
Flying and teaching techniques
vary widely in our hobby, and vary from one instructor to another.
The goal of this document is to encourage some standardization and provide a practical minimum amount of knowledge.
Page 4

## Slide 5: Contents
Section 1: Getting Started, Field Rules and Safety
Section 2: Selecting your training airplane and radio
Section 3: How Training Works
Section 4: How planes fly
Section 5: Flying Lessons!! (Flight Instruction and Flying Technique)
Section 6: Radios and ESC’s
Page 5
Notes: I have included hyperlinks to each one of the sections.

## Slide 6: Section 1
Getting Started, Field Rules and Safety
Page 6

## Slide 7: 3 Things to Do Right Away Note: You may come the first time to training without doing these
1. Get your AMA NUMBER - FREE if under 18
      Academy of Model Aeronautics http://www.modelaircraft.org
      Provides liability insurance (required by King County)
      AMA will send you your membership number in several days
Apply for MAR/C membership on our website (you need your AMA membership number before doing this) FREE if under 18
Page 7

## Slide 8: Preparation Checklist
Visit the field anytime, talk to members, see the planes (optional, but recommended)
AMA membership
MAR/C membership (apply as soon as you have AMA number)
Read sections 1-4 and Phase 1 of section 5
Purchase your plane and transmitter AFTER reading section 2
Read instructions for your plane, charger, and batteries
Assemble your plane according to the instructions
Come to training night with your batteries recently charged
Page 8
Do these as soon as possible

## Slide 9
Use the Ground School!!
Easy reading
What to buy and not to buy
Lesson material for each phase of your flight lessons
Guardians and Students – read section 1 now
J
Join AMA
Learning Tools
on our Website
http://www.mar-c.org/training

## Slide 10: Safety Propellers can cause Significant Injury
Before plugging in the battery of an Electric Aircraft, ensure that:
  Transmitter ON
  Throttle is at idle
  Throttle Cut switch is in “cut” position
  Airplane switch (if so equipped) if OFF
  Hands and arms are away from the propeller
When starting Glow or Gas engines, ensure that:
  Transmitter is ON
  the Aircraft is restrained
  no one is standing to the side or in front of the prop in case the prop comes loose.
Ensure your propeller nut remains tight.
    Wooden props especially tend to loosen with time
    Gas and glow engines can “kick back” during start attempts and suddenly loosen the prop nut
Page 10

## Slide 11: Safety: LiPo Batteries
LiPo batteries can catch fire if not treated properly.
Always charge batteries in a fire-proof container like a flower pot or a Lipo bag. Never charge inside a car.
Read all the warning material that comes with your charger and battery. Charge at the recommended current or “C” rate.
Always fly one flight only with a fully and freshly charged battery
Never run the battery all the way down. This will damage the battery. Make sure at least 25% is left. Use the battery checker after each flight to learn how many minutes of flight the battery is good for. Use count-down timer to limit the time of every flight.
Do not store your batteries for more than a few days fully charged. This will limit their life.
Understand your charger. When charging a battery ensure that you have the polarity on the battery correct before charging. Red goes to red and black goes to black.
Consider investing in a good charger that can tell you how many milli-amp-hours (maH) are put in each time a battery is charged. Compare this to the rated maH of the battery
Page 11
Battery Checker
Ceramic Flower Pot, or
LiPo Safe Bag
Charger
connections
FIRE SAFETY

## Slide 12: A Rule for Real Aircraft we can Learn From
Federal Aviation Administration (FAA) 91.3, Responsibility and authority of the pilot in command: (a) The pilot in command of an aircraft is directly responsible for, and is the final authority as to, the operation of that aircraft.
Page 12
Notes: Link: http://rgl.faa.gov/Regulatory_and_Guidance_Library/rgFAR.nsf/0/e63bbedc3044a110852566cf00612076!OpenDocument

## Slide 13: Rules enhance fun and cooperation, and ensure that we keep our field.
Marymoor R/C Club: Field Operating Rules
Academy of Model Aeronautics: AMA Document 105 - Safety Code
US Federal (FAA) rules for flying RC aircraft
  Read “Know before you Fly” to understand WHERE and when it is legal to fly:
        http://knowbeforeyoufly.org
Page 13

## Slide 14: A few of our Field Rules
Flyers less than 12 years of age and all Provisional Category (yellow badge) members must fly under the supervision of a fully qualified MAR/C member
Fly from a fenced pilot station only
No flying over the pits (anywhere behind the fenced pilot stations)
Takeoffs and hand launches from the runway only
Callouts make for safe flying – see signs at each flying station
All injuries and accidents need to be reported.
Read the full set of MAR/C rules on the GIANT sign upon entering the pit area.
Page 14

## Slide 15: Section 2
Selecting your training airplane and radio
Page 15

## Slide 16: Recommended Airplanes Available at Redmond Hobby Town (along with good advice)
Electric power is strongly recommended for training
Wheels large enough to take off from grass (2 ½ inches diameter). Apprentice airplanes need upgraded wheels
High Wing with dihedral
Ailerons required for our program
Nose wheel or tail wheel landing gear are OK. Tail wheel is better on our grass field and more durable.
Page 16
Park-Zone Sport Cub
E-Flite Apprentice
Notes: Selecting An Airplane
An airplane specifically designed for training and usually called a trainer is the best type of for student pilots to use. These trainers generally have a wing that mounts on top of the fuselage, and wing dihedral (wing halves form a slight “V” shape when viewed from front or back). This type of airplane has a tendency to fly level when the control sticks on the transmitter are released.
Your airplane must have four control channels (throttle, aileron, rudder and elevator) to be used in the training program. Additionally, your transmitter must have buddy box capability - note that some transmitters do not.
Trainers may be purchased as Ready To Fly (RTF), Almost Ready To Fly (ARF) or as a kit, and may be powered by “glow” model airplane engines or by electric power.
RTF (Ready to Fly)
Usually the cost of an RTF is significantly less than the cost of purchasing all of the required components (airplane, radio, engine or electric motor & electronic speed control, etc.) separately. Additionally, the components have been selected by the manufacturer to be compatible with each other. Typically it takes an hour or 2 to assemble an RTF so that it is ready to fly.
Two RTFs used in the training program that have been were successful:
The Hangar 9 Alpha 40 is designed for a “glow” engine or electric power and includes everything required to fly the airplane except for the engine (or electric motor), glow fuel, fuel pump, glow plug igniter & battery charger. This airplane is no longer available with the engine installed.
The E-Flite Apprentice has an electric motor and includes everything required to fly the airplane. List price is approximately $300. It is recommended that a second flight battery be purchased for as well. This will allow a pilot to make 2 flights. Additionally, charging of the battery used for the first flight may be started soon after the airplane lands and it can be used for the third flight.
Alpha 40 Eflite Apprentice
ARF (Almost Ready to Fly)
An ARF contains the parts required to assemble an airplane; however, the radio, engine or electric motor, ESC (electronic speed control) and other components must be purchased separately. This can be an advantage. For example, a more versatile and capable radio than the ones provided with the 2 RTFs above would have 6 channels, end point adjustment, dual rates and memory for several different models.
Typically ARFs contain the following: 2 wing halves & 2 ailerons, nearly completed fuselage, vertical stabilizer & rudder, horizontal stabilizer & elevator, motor mount, wheels and other parts. A manual is provided that contains detailed steps that show how to assemble the airplane and install the radio and engine or electric motor. Usually an ARF can be assembled and ready to fly in about 16 hours. More insight into airplanes, radios and engines or electric motors will be gained by assembling an ARF than purchasing an RTF. Three examples of available ARFs are
the SIG Kadet LT40 EG (electric or glow power)
Tower Trainer 40 Mk II ARF (glow),
the Hobbico Avistar Elite .46 GP/EP ARF (glow or electric).
Purchasing quality components such as engines, motors, speed controllers, servos, etc offers the possibility that these components can be used on future projects after the student graduates from the trainer.
Sig LT 40 Tower Trainer 40 Mk II Hobbico Avistar Elite
Kits
Kits take the most time to build, typically 80 hours, but are also the most rewarding because there is a great sense of achievement in completing one. The covering is not included in the kit, so a unique color and trim scheme can be developed by the builder. Like an ARF, the radio, engine, motor, ESC and batteries are not included and must be installed.
A set of plans, usually one sheet for the wing and one sheet for the fuselage, and an assembly manual are included. Assembly starts by placing one sheet of the plans over a building board and then covering the plans with waxed paper or plastic wrap. Next a spar is pinned over the plans and the wing ribs are glued to the spar. There are many parts that must be glued together to complete the wing and then the fuselage. Once the airplane is completed, the builder will have a lot of knowledge and skill about how airplanes are constructed and should be able to make repairs to this airplane and other airplanes in the event that they are damaged in a crash. This type of insight is not gained by assembling an RTF or ARF. Three examples of kits are the
Sig Kadet LT40 kit
Carl Goldberg Eagle 2
Great Planes PT-40 Mk II Trainer.
Electric Power vs. a “Glow” engine?
Many prospective students ask which is better; a glow engine or electric power? It boils down to personal preference, but our experience is that there is less time lost due to tinkering with the engine if the student selects electric power. Are you excited about the throaty sound of an internal combustion engine or do you prefer cleaner and quieter electric power? Both require knowledge and practice to be successful. Both require some investment in field equipment and tools, but different, as we explain in other links.
Electric power is sometimes associated with smaller size, but this is not necessarily so. Larger, heavier trainers handle better in gusty and windy conditions. In the RTF examples, the Alpha is larger and heavier than the Apprentice. But in general, for similar sized trainers it does not matter whether the airplane is glow or electric powered.
If you choose “glow” or gasoline engines, be aware that they require more attention and time to mixture settings, glow plugs, fuel flow and fuel system leaks, starting procedures, and other details that can be time consuming and downright vexing during the training process. Used “bargain” engines often require very high levels of time and attention, and perhaps replacement of parts before they will start and run reliably.

## Slide 17: Selecting a Transmitter
MAR/C Training program provides the “buddy box” transmitter.
You must own a Spektrum or Futaba brand transmitter to be compatible with the club buddy boxes, or you must provide your own buddy box
A simple transmitter might be supplied with a “Ready to Fly” (RTF) model like the Apprentice
Better ones with more channels are a good investment if you are sure you will stick with the hobby
Protect the switches and sticks by storing it in a case or a plastic box with padding
Page 17
Notes: Your Transmitter
Depending on the radio transmitter you select, it will be powered by AA batteries or a rechargeable battery pack. If rechargeable, the charger will be supplied with the transmitter. It is critically important that the transmitter battery be fully charged before coming to the field.
Whether simple or sophisticated, transmitters must be protected from damage during the ride to and from the field. Small switches and antennas can be fragile. An old briefcase or a large Tupperware type container lined with some padding can meet this need.
As mentioned in the Selecting and Airplane link, a simple transmitter may be supplied with an RTF (ready to fly) package. If the student purchases an ARF (Almost Ready to Fly) or a kit, they have the latitude of purchasing either the simple transmitter or stepping up. A so-called “computer” transmitter allows more clever ways of setting control throws and sensitivity, as well as mixing controls so that for example moving the aileron stick can result in both ailerons and rudder moving. Transmitters of this type are appropriate if the student is confident of sticking with the hobby beyond initial training.
A transmitter left ON before coming to the field, or accidentally switched ON while packing up to go to the field could result in a dead battery and if not discovered, possible loss of control of the airplane. You should check the battery voltage indicator on the transmitter before each and every flight. Try using this checklist just before each takeoff – B A T T:
Battery(s)
Antenna (extended or aligned correctly)
Trim (transmitter control trims set)
Timer (be ready to time your flight)

## Slide 18: Power Options
Electric Motor (strongly recommended for training)
    Must understand safe charging and storage of Lithium-Polymer (LiPo) batteries.
Internal combustion “gas” engines (not recommended)
    Traditional “Glow” model airplane engine
    New small gasoline ignition engines
    Require different field equipment than electric
    More difficult to achieve reliable operation
    Must have a sound check inspection – 90db is the limit
Page 18

## Slide 19: Electric Power Support Equipment
  Arrive at training with 3 fully charged batteries, or 2 fully charged batteries and a charger.
  Recommended:
      Battery checker for checking the charge status of a battery before and after the flight
      A charger that can tell you about health of the battery (upgrade from the one supplied with an Apprentice)
Page 19

## Slide 20: Section 3
How Summer Tuesday Night Training Works
Page 20

## Slide 21: Your First Day of Training
A little check-in paperwork
Our Tech Inspectors check out your airplane before it flies.
Meet an instructor.
Learn about the “Buddy Box” system that connects two transmitters so that your instructor can ensure safe flying
Your first flight using the club trainer, or your own airplane
Page 21
Notes: What is training like?
A MAR/C tech inspector will check each airplane used during training to ensure that it has been assembled correctly and is flight worthy according to the MAR/C Pre-Flight Checklist. Most deficiencies identified by the tech inspector can be corrected quickly at the airfield.
Student pilots will fly with different MAR/C instructors during training using a “buddy box” system that employs two transmitters connected by a special wire. The instructor has the ability to fly the airplane, and take control instantly at any time. The instructor will hold the transmitter that goes with the airplane, and the student will hold the “buddy box” transmitter.
Initially, the instructor will perform all take offs and landings. The instructor will transfer control of the aircraft to the student when it is at altitude and flying straight and level. At first, the student will usually not be able to fly the airplane very long before the instructor needs to make a correction. As experience is gained, the student will be able to fly the plane with few corrections from the instructor. Eventually the student will progress to taking off followed by landing. The student will also learn how to recover from adverse situations such as being upside down. A log book is used to document the progress of each student. In the final steps of the program, 2 instructors observe 2 flights that are required to be successful without any corrections by the instructors. The last flight is a solo flight without use of a buddy box which must be successfully completed without help from the instructors. Each graduating student receives a certificate attesting to their proficiency and receives a full membership card to replace their provisional card.

## Slide 22: Your Own Plane -
After your introductory flight on the club trainer, you will be expected to have your own equipment:
        Plane
        Transmitter
        Extra batteries and/or charger if electric
        Appropriate ground equipment for your plane
Before coming to the field with your plane, assemble it to the best of your ability. Follow instructions carefully.
Before flying any new plane, a MAR/C Tech Inspector will examine your plane using the checklist on the next pages
Page 22

## Slide 23
Intentionally left blank

## Slide 24
Page 24
Before flying, a MAR/C Tech Inspector will check your plane using this checklist

## Slide 25
Page 25
Before flying, a MAR/C Tech Inspector will check your plane using this checklist (page 2)

## Slide 26: Early Flights
When you begin your flights, your instructor will walk you through a pre-flight inspection or ask you about your inspection.
Instructor will taxi your aircraft.
Instructor will take-off and depart the runway.
Once your aircraft is trimmed the instructor will turn the aircraft over to you
Page 26

## Slide 27: Training Expectations
Every Tuesday evening check out your logbook and a buddy box.
Get your name on the instructor waiting list
Meet with your instructor
    Ask questions!
    Instructor will ask about your progress. Tell them what phase you are working on (see section 5)
    Make a plan for the upcoming flight
After each flight, get your name on the list to be assigned to the next available instructor. You will likely fly with a different instructor each flight
Return the logbook and buddy box after your last flight of the evening
Page 27

## Slide 28: When are you Done?
A solo flight and quiz, when you are ready. See end of section 5 for details.
Most solo near the end of the summer.
After you pass, you are a “Youth”, or “Full” (adult) member, and may fly by yourself without buddy box and instructor.
However, pilots less than 12 years of age must be supervised by an adult, full club member
Use of computer RC simulators is highly encouraged. Students learn faster, especially in the early stages.
    Great Planes Real Flight v. 7
    Horizon Hobbies Phoenix R/C flight sim
    For Mac computers, Aerofly RC7
Good pilots never stop learning!

## Slide 29: Section 4
How the planes fly
Page 29

## Slide 30: Controls, Aerodynamics, and Stability
Elevator, Rudder, Aileron
Wing planform
Lift and Wing Design
Wing section (airfoil)
Tail group (empennage)
Center of lift, center of gravity
Characteristics of a “speed stable” airplane
Page 30

## Slide 31: Ailerons, Elevators, and Rudder Control Roll, Pitch, and Yaw
Ailerons
  Roll, left and right
Elevators
  Pitch, up and down)
Rudder
  Yaw, left and right
Page 31
Notes: LATERAL CONTROL, AILERONS.
Ailerons are moveable control surfaces mounted on the trailing edge of both wings. They control the rolling plane of the aircraft. They are deflected differentially.
As the ailerons are deflected differentially by pilot control input from their neutral position, (one up, the other down), they alter the airfoil camber, either in positive or negative sense, and therefore increase or decrease the lift coefficient of the airfoil and, of course, the drag coefficient, and thereby roll the aircraft.
In the case of the downward deflecting aileron the increased positive camber produces increased lift, and also the associated increased drag, whereas the other aileron, defecting upward has the opposite effect, producing reduced lift and reduced drag. The unfortunate result is that the differential drag produces an unwanted yaw in a direction opposite to the commanded roll. This is termed Adverse Roll.
Adverse roll is most widely countered by setting up the ailerons such that the downward deflecting aileron has less travel than the upward moving aileron, so that the downward deflecting aileron is operating in that range of the L/D curve where the rate of increase in lift coefficient is far greater than the rate of increase in the drag coefficient. Conversely the upward moving aileron, with it's greater deflection reduces the lift coefficient and to a greater extent, the drag. This setup is termed "Differential Ailerons". For example, an aircraft might be set up with the upward deflection of the ailerons at 30 degrees maximum, and the downward deflection at 15 degrees maximum.
An alternative is the use of "Frise Ailerons", a design wherein the aileron hinge line is a short distance aft of the aileron leading edge, and leading edge of the upward deflecting aileron is deflected down and exposed beyond the surface of the underside of the wing, thereby creating drag. This drag acts to oppose the drag associated with the increased lift created by the downward deflecting aileron on the other wing. Adverse yaw is reduced or eliminated. A further refinement of the Frise aileron design allows the protruding leading edge of the negative lift aileron to scoop positive pressure airstream from the lower surface of the wing and eject it upward through a contoured slot between the leading edge of the aileron and the wing into the airstream passing over the upper deflected body of the aileron. This jet of high-energy air enhances the effectiveness of he upward deflecting aileron.

## Slide 32: Radio Controls
Page 32
Ailerons
(roll)
Elevator
(Pitch)
Rudder
(yaw)
Power
Trim Controls

## Slide 33: Wing Planform
Rectangular (best for trainers)
Tapered
Elliptical
Swept
Delta
Page 33

## Slide 34: Lift
Lift comes from:
    Angle of Attack
    Wing Area
    Airfoil Shape
    Airspeed
In level flight, Lift = Weight
Page 34
Direction of flight
Lift
Drag
Weight
Notes: PURPOSE
The function of the wing in conventional aircraft is to provide the aerodynamic lift necessary for flight. Control surfaces, ailerons, are mounted on the wing to provide control over the rolling plane of the aircraft.
ESSENTIAL REQUIREMENTS FOR AERODYNAMIC LIFT
Aerodynamic lift is generated by the flow of air over the upper and lower surfaces of the wing as it moves through the air propelled by the motive force of the rotating propeller, jet engine, or, in the case of sailplanes, gravity.
The rate of forward movement through the air, the airspeed, must reach a certain minimum value in order for the wing to generate sufficient lift for to overcome the mass of the aircraft and achieve flight.
The wing must have an appropriate cross sectional shape (in the fore and aft direction), called the Wing Section, or Airfoil Section, in order to generate aerodynamic lift.
The wing must also have adequate wing area, the product of span, (wingtip to wingtip dimension) and chord, (the mean width of the wing in the fore and aft direction). The relationship between span and chord is termed the aspect ratio.
AERODYNAMIC LIFT
An aircraft wing creates lift from the flow of air over both it's upper and lower surfaces. The much larger lift component is produced by the airflow over the upper surface of the wing, the negative-pressure lift. The flow over the undersurface of the wing, the positive-pressure lift, produces a minor component of the total produced and only at positive angles of attack.
The negative-pressure lift, from the upper wing surface, is produced only between a fairly narrow range of Angle of Attack. The angle of attack is the angle between the chord line of the wing and the undisturbed airstream vector impinging upon the wing. A typical range, for a wing of fully symmetrical (uncambered) airfoil section is approximately 0 to +15 degrees. A wing of cambered airfoil section will generally produce a higher lift coefficient than it's uncambered cousin, but will have a slightly different range of lift producing angle of attack, approximately -5 to +12 degrees.
The positive-pressure lift continues to be produced at very large angles of attack, but as drag at such attitudes is so large, this lift is of little practical value.
As an aircraft wing generates lift, it also generates drag; a force acting to retard forward movement. As the angle of attack increases, so do both lift and drag, but at a different rate, lift increasing initially at a greater rate than drag, but drag increasing dramatically at the upper range of angle of attack.
WING DESIGN
The interplay of lift and drag has resulted in aircraft designers adopting many different combinations of wing section, planform, area and aspect ratio. The planform shape of the wing, rectangular, tapered or eliptical is another variable utilized by designers.
Aspect Ratio is the ratio of wingspan to chord. For most RC model aircraft the aspect ratio found to be a good balance between ease of construction and aerodynamic efficiency is between 5 and 6; for example, an aspect ratio of 5 means that an aircraft of 60" wingspan would have a chord of 12".
For simplicity of construction most RC model aircraft designers opt for a rectangular rather than tapered or elliptical planform for powered aircraft. This choice is not the aerodynamic optimum, either for lift distribution or induced drag considerations, however most RC Model aircraft are very adequately powered, so that, in most cases, the drag associated with the aerodynamic lift of the wing is less important than it is in the case of full-sized aircraft. For sailplanes the optimization of the lift/drag couplet is very important and therefore wing planforms, aspect ratio and airfoil sections are usually radically different from those on powered aircraft.
An important consideration for any aircraft designer is the Reynold's number envelope in which the aircraft will operate. The Reynold's number, abbreviated to RN, is a non-dimensional number derived form a mathematical expression whose variables include air density, airspeed and the chord dimension of the wing. It is used as a yardstick in wing section analysis and selection. The aerodynamic regime in which we operate our model aircraft is commonly referred to as Low RN Aerodynamics.

## Slide 35: Lift is greatly reduced when the Wing Stalls
Stall can occur when:
    Too slow
    Pulling too much up elevator
    Steep bank angle
    Any combination of these three
Occurs at critical angle of attack, about 15 degrees
Trainers have gentle stall characteristics. The warbird you want to fly someday might not.
One wing can stall before the other, resulting in a sharp roll, and if it continues, a spin. A good trainer won’t do this.
Page 35
Notes: THE STALL
AN ACCIDENT
The RC model aircraft, a warbird scale model of fairly high wing loading, is on the downwind leg of a left hand landing pattern, flying with a modest tailwind so that it's groundspeed is a little higher than the pilot prefers, so he throttles back and the model's nose drops. He adds a little up elevator to maintain altitude. He turns left onto base leg, banking quite steeply because the tailwind is pushing the model downwind, elongating his pattern. He adds up elevator in the turn to maintain altitude, simultaneously reducing power. He trims the nose up on his base leg, slowing the aircraft. He turns left again, onto final, once again banking quite steeply, about 45 degrees, into the wind and makes his final power reduction. The aircraft is now experiencing a fairly high positive G load and is decelerating. The nose drops in the turn, so the pilot reacts with corrective right aileron and up elevator. The left wing, with the aileron deflected downward, exceeds the critical angle of attack and the lower, left wing, tip-stalls, the aircraft inverts, the nose drops vertically and before a spin can develop the aircraft impacts the earth disastrously. This scene has been repeated many times, tragically, and usually fatally, in full-size aviation, and embarrassingly in model aviation.
WHAT HAPPENED?
When a wing assumes an Angle of Attack, either positive or negative, in excess of the lift-producing range previously described, the airflow no longer conforms predictably to the upper curvature of the wing's surface, but separates and becomes very turbulent. Virtually all lift is lost, and drag increases dramatically. Very often aileron control is jeopardized and the aircraft departs from controlled flight. It has stalled, and is no longer flying, but simply dropping.
It is not low airspeed, but exceeding the wing's critical angel of attack, that induces total flow separation over the upper surface of the wing; the stall. When the pilot of an aircraft attempts to avoid loss of altitude at low airspeed by raising the nose of the aircraft, and therefore increasing the angle of attack, he is in danger of stalling the wing.
WHY?
In any aircraft, model or full-size, the behavior of the wing at critical high angles of attack is most important. As the aircraft's angle of attack approaches the critical value, and stalling is imminent, it is important for continued controlled flight that the wing should not experience tip-stall. If asymmetrical tip stall does occur, the aircraft will abruptly drop the stalled wing, yaw violently towards the stalled wing, and very possibly enter a spin. Many aircraft use wing Washout, a wing twist, to allow the outboard portion of the wing to continue to experience non-critical angle of attack while the inboard section becomes critical, and stalls. By this means aileron control is preserved, to a certain degree, and spinning is avoidable.
Some aircraft also vary the Airfoil Section from root to tip, using cambered section at the root, for higher lift, and non-cambered section at the tip, for higher critical angle of attack.
The Planform Shape of a wing also influences the behavior at the stall. Strongly tapered planforms, where the wingtip chord is significantly less than the root chord, and therefore the Reynold's Number of the tip is much lower that the root, are more subject to tip stall than less tapered, or non-tapered planforms.
At the outboard tip of a wing in flight a strong vortex forms, with overpressure air from the underside of the wing curling up around the wingtip into the underpressure topside of the wing. This vortex creates significant drag and by it's disturbance of the airstream on the top surface of the wing at the tip, reduces the effective aerodynamic span of the wing. Designers have used a wide variety of devices to minimize the drag and span-reduction effects of the tip vortex; winglets, end plates, Hoener shapes and several others. Perhaps the most elegant solution is the adoption of an eliptical planform, such as was used in the Supermarine Spitfire so that the vortex becomes very small and the span-wise lift distribution of the wing is optimized with respect to imposed structural bending moment loads. The Spitfire's wing has a beautiful shape but it is, unfortunately, complex to design and build.
Among the very wide range of RC model aircraft flown today, those of foam construction, with powerful electric motors, have very benign stall characteristics. They generally have very light wing loading and high power loading, so that they perform some remarkable maneuvers with the wing in a fully stalled condition, flying on overpressure lift from the underside of the wing and propeller thrust.
Similarly, the typical trainer has quite low wing loading, and fairly gentle stall behavior. They are designed very carefully to avoid tip-stall, and to keep recovery from the stall simple with no departure from controlled flight.

## Slide 36: Airfoil Shapes
Page 36
Flat bottom airfoil
much camber (mid-line is curved)
Often used on trainers and Cubs
Good at low speeds
“Semi-symmetrical” airfoil
has some camber
sometimes used on trainers
Good all-around airfoil
Symmetrical wing
Zero camber - mid line is straight
Used on aerobatic airplanes
Notes: WING SECTION.
Wing section, or airfoil, is the term used to describe the geometric shape of a cross section of the wing in the fore and aft plane. Wing Sections are assigned names by their developers, for instance, the wing section called NACA 2412 is just one of the many developed by the National Advisory Committee for Aeronautics, a US Federal Government agency now part of NASA.
Wing Sections are all geometric variations of a streamlined teardrop shape. Sometimes they are fully symmetrical, meaning that they do not have camber. Camber is the term used to describe any curvature of a midpoint line joining the extreme points of the wing section at the leading and trailing edges.
Model aircraft designers frequently choose Wing Sections from a vast array available from many sources, such as NASA, rather than develop their own Wing Sections. The Airfoil Section mentioned above, NACA 2412, is a very widely used section. It is one of NASA's four digit series, where the first digit, 2, indicated that the section has camber of 2% of total depth. Second digit, 4, indicates maximum camber located at 40% of the chord. The last two digits indicate airfoil maximum thickness, 12%.
Wing sections are selected by the model designer to suit the intended use and flight characteristics of the model. The aerodynamic characteristics of most wing sections are described mathematically in a series of graphs commonly known as Lift/Drag graphs, or L/D curves. These graphs are the result of wind tunnel tests. As the name implies, these graphs plot the lift coefficient produced by the subject wing section against the induced drag and pitching moment coefficients as the angle of attack is varied.
At any specified airspeed and angle of attack the lift of the subject wing may be calculated using the Lift Coefficient from the L/D graph in a series of mathematical expressions. Similarly the Induced Drag, which is the resisting force resulting from the Lift generated by the wing having the subject Section at a particular airspeed and angle of attack, may be calculated.
Model designers typically choose fully symmetrical wing sections for aircraft intended for aerobatics. Such wing sections are equally effective inverted as they are upright. Model aircraft intended for less inverted flight generally use airfoils having some camber as such airfoils generate higher lift coefficients than do symmetrical airfoils at positive angles of attack.
Section thickness is another variable. Thin sections have lower induced drag than thicker sections, all other factors being equal. Practically, for RC model use,
a reasonably thick wing section between 10 and 14 percent of chord provides for adequate depth of spar, (to resist imposed loads in flight), and ease of construction. Thinner wings are used for high speed applications where low drag is important, such as pylon racers or turbine powered aircraft.

## Slide 37: Empennage (The tail Group)
Large tail surfaces, longer aft fuselage, and relatively small elevator and rudder result in a smoother, more stable airplane.
Page 37
Notes: The Empennage is the term often used to describe the tail group of an aircraft; the horizontal fixed stabilizer, the movable elevator control surface, the fixed vertical stabilizer and the movable rudder control surface.
In conventional aircraft the empennage is positioned aft of the wing and mounted at the aft end of the fuselage. The distance between the center of lift of the wing and the center of lift of the horizontal tail group is called the tail moment arm.
The horizontal group, (stabilizer and elevator), act in flight to counteract the pitching moment of the wing airfoil and control the aircraft in the pitching plane. The stabilizer is fixed at a slight negative angle of incidence with respect to the wing such that in level constant airspeed flight the downward aerodynamic force acting upon the horizontal tailplane group balances both the downward pitching moment of the wing airfoil and the usual placement of the longitudinal center of gravity slightly ahead of the wing's center of lift.
The horizontal group airfoil is normally uncambered, operating at a slight negative angle of attack in level stable flight. The movable elevator surface, when deflected, creates a momentarily cambered airfoil, and hence either positive or negative lift, and therefore alters the pitch attitude of the aircraft.
The vertical tail group functions in exactly the same manner to control the yawing plane of the aircraft.
The empennage act much like the tail feathers of an arrow, to damp and eliminate pitch and yaw disturbances from level flight caused by air turbulence. In order to achieve this damping effect, the center of lateral area of the aircraft's fuselage and vertical fin must be slightly behind the center of gravity of the aircraft.
The empennage, in particular the vertical component, contribute to spiral stability when the fin area is carefully chosen and located.
The empennage is strongly influenced by downwash from the wing and by the spiraling slipstream of the propeller. The downwash is a variable condition, depending upon airspeed and angle of attach of the wing and the resultant trim changes are usually countered by control input from the pilot.
When the fin is positioned above the thrust line of he engine the spiral slipstream from a normally rotating propeller impinges upon the left, port, side of the fin with an angle of attack that produces lift the right, starboard side, resulting in a yaw to left, or port. The spiral slipstream can be partially reduced by an angular offset of the engine's thrust-line, usually to the right, starboard side, so that the slipstream impinges upon the fin with an zero angle of attack.

## Slide 38: Balance and Pitch Stability
A stable trainer type airplane will have the balance point, or center of gravity (CG) ahead of the center of lift.
ALWAYS make sure your model balances at the point recommended by the manufacturer.
Page 38
Notes: Longitudinal Balance.
The correct positional relationship between location of the center of gravity of the aircraft and the center of lift is critical for stable flight. The center of lift produced by the wing varies depending upon the airfoil section of the wing, but is generally located about 30-40% of the wing mean aerodynamic chord. The center of gravity must be slightly ahead of the center of lift, say about 5% ahead. This arrangement then requires a slight downward force, negative lift, to be applied by the horizontal tailplane to balance the downward pitch couple resulting from the CG/CL relationship.

## Slide 39: Roll Stability
Dihedral effect helps to right the airplane in roll, making it easier to fly
Page 39
Dihedral angle
A zero dihedral high wing airplane will still have some dihedral effect
Swept wings have dihedral effect
Aerobatic airplanes usually have zero dihedral so they also fly well upside down
Notes: Lateral Balance.
The aircraft must be balanced laterally in order to achieve stable, "hands off" level flight. It is possible to correct for lateral imbalance by use of aileron trim, but only within a narrow airspeed range. A model that is so trimmed will not track properly in maneuvers involving airspeed variation.
STABILITY AND TRIMMING
Trimming for flight is the process of adjusting all the forces acting upon the aircraft in flight in order to achieve stable 'hands off" flight. The forces are lift, both from the wing and from the horizontal tailplane; thrust, both quantity and vector; drag; and gravity, acting through the CG.
Accurate airframe construction is essential for proper trimming. Warped, mis-shapen or twisted models cannot be properly trimmed. When an aircraft is accurately built trimming is largely a process to ensure that control surfaces are truly neutral at rest and that the CG is correctly located, and that engine trust vector is in accordance with the design. An accurately built model will fly straight and level without significant control surface trim adjustment.
Aircraft can be trimmed for strong positive stability, such that they will recover quickly from any disruption of level flight, either in pitch, roll or yaw and return to that condition without pilot control input. Such aircraft are termed strongly auto-stable in flight. Good examples are soaring sailplanes, with their polyhedral wings, and most trainers.

## Slide 40: Section 5
Flying Lessons!!
(Flight Instruction and Flying Techniques)
Page 40

## Slide 41
MAR/C
R/C FLIGHT TRAINING
STUDENT
LOGBOOK
Student Name_______________________________
AMA# _________________ FAA# __________________
Phone Number______________________________
Page 41

## Slide 42
Page 42
Training Log used byYour Instructor
Phase 1 – Pre Flight and Taxi
Phase 2 – Basic Orientation and Pattern
Phase 3 – Approach and Landing
Phase 4 – Takeoff
Phase 5 – Advanced Orientation

## Slide 43: Phase 1 Pre-Flight and Taxi
Pre-Flight Inspection
Before Takeoff Checklist
Taxi
Callouts
Phase 1
Page 43

## Slide 44: Pre-Flight Checklist
Before before powering up on every flight, you, the student, should check at least the following:
    Radio installation secure (before you close up the plane)
    Wing secured with proper number of rubber bands
    Control surfaces secure: Linkages, hinges, and servos
    Engine & Prop: secure, prop not damaged
    Electric: Recently charged and fully charged battery, well secured in the plane
    Gas or Glow: Check fuel hoses secure, tank full
    Do a range check, before a model’s first flight, or if any part of the radio installation has changed
Note: This checklist is not the same as the much more comprehensive pre-flight inspection checklist that we use before the first flight of your airplane with the training program. This checklist is a shorter version for you to use before every flight
Page 44
Phase 1

## Slide 45: Before Takeoff Checklist
This habit will save your airplane someday
After the plane is powered up, but before taking off:
    Battery (transmitter battery “in the green”)
    Antenna (transmitter antenna placement
    – NOT pointed at the airplane)
    Trims – set correctly
    Timer – ready to be started, right amount
    Controls – Check operation and DIRECTION!
    Do Controls check for both student and instructor
Page 45
Phase 1

## Slide 46: Tell Other Pilots What you Intend using Standard Callouts
“Coming out on the left” (or right)
“Taking off Left to Right” (or Right to Left)
“On the Field” and “Clear of the field” (for a person)
“Airplane on the Field” (stuck or engine quit)
“Touch and Go from the Left” (or Right)
“Low pass from the Left” (or Right)
“Landing from the Left” (or Right)
“Field Clear” (after you or your plane is off the runway)”
“Deadstick, Deadstick” (engine failed, need immediate landing)
Page 46
Phase 1
Notes: We enjoy, at Marymoor RC Club, a magnificent flying field, conveniently located, extremely well managed, and with a minimum of controls and restrictions.
We also enjoy a wide variety of RC modeling interests among our membership, and that is reflected in the wide variety of model types to be seen at our field on a fine day.
In order that we might continue to enjoy relatively uncontrolled flying at our field it is apparent that we must adhere to some basic courtesies and conventions to avoid friction between flying members and promote safe operation of our models.
Mandatory Rules and Regulations.
We must be aware of, and fly within the designated limits established by our agreement with King County.
We must be aware of, and comply with the MARC noise restriction criteria.
We must be aware of, and abide by the various AMA and MARC Safety Rules.
The following are suggested Courtesies and Conventions to be followed at the flying field:
Be aware of the very different characteristics of models at our field. Fast flying, heavy models do not mix well with lightweight foamies, or with electric 3D models doing their typical hovering maneuvers, or with helicopters. Choose when to fly, based upon the characteristics of the other models in the air, choose to fly with compatible models. A typical flight, for most models, is only about 10 to 15 minutes, so waiting for the best mix of models is not vary onerous.
Flight Line Conventions.
When flying a model we must, as a courtesy, call out our intentions loudly enough that flyers at all flight stations hear and understand. The announced intentions are, for example:
Taxi, or carry, the model from the pit area to the Hold Short position, on the taxiway, just short of the strip. Place or position the model in the 'Hold Short' position, about 5' from the edge of the strip.
Check that no model is in the landing approach before calling "Coming out", a call before taxing out onto the field for take-off from the Hold Short position. Listen for either acknowledgement and/or alert calls from other flyers.
Taxi onto the field if no alert call from other flyers. Taxi to the take-off position, hold, check for traffic, then call "Taking off, left to right", or "Right to Left" depending on prevailing traffic pattern.
Take off, climb out and enter the traffic pattern, or exit the pattern to the aerobatic area clear of the pattern.
If for any reason, an aborted takeoff is necessary, call it out loudly, "Abort, abort". Either taxi the model to the nearest taxiway exit, or if required to enter the field to retrieve the model, check for traffic, and as soon as possible call out "Entering the field". Wait for affirmative acknowledgement, then quickly enter and retrieve model.
In the pattern, fly the downwind leg clear of the far side of the field at about 100' altitude. Fly crosswind legs clear of the approach and departure strip thresholds.
Maneuvers. Fly aerobatic routines clear of the traffic pattern, unless there are no other models in the air at the time.
Call out your intended maneuvers in the pattern before executing, such as "Touch and Go", "Low Pass Flyby", "Landing, Full Stop" or most urgently and loudly, "Deadstick, Deadstick, Deadstick"
In the event of a successful dead-stick landing on the strip and before entering the field to retrieve the model, check for traffic, and as soon as possible call out "Entering the field". Wait for affirmative acknowledgement, then quickly enter and retrieve model.
When exiting the field with the model. call "Clear of the Field"
If it is necessary to traverse the field to recover a model from the rough beyond the strip, check for traffic, and if clear call out loudly, "Entering the field," wait for affirmative response, then quickly traverse the field and commence the search for the downed model.
While a retrieval party is traversing the field, other flyers should fly high and clear of the field. Flyers should maintain awareness of the location of the retrieval party, particularly if they are in close proximity to the field, and fly, at all times, clear of them.
Upon return from the downed model retrieval, the party should check for traffic, call clearly and loudly, "Entering the field", wait for affirmative response, and then traverse the field as quickly as possible, and once across the field, call "Clear of the field"
Pit Area conventions.
When the pits area becomes crowded electric model flyers should avoid using the engine start tables.
Use of more than one set-up table per flyer is discourteous on busy days. Store multiple models under the table, rather than on adjacent setup table, or engine start tables.
Non-members of the club may be invited as guests of a club-member to enter the pits area, but they are the responsibility of the club member. Guest should not include small children or pets. Guests may not accompany the club member to the flightline
It is courteous to cleanup before departing the field at the end of a flying session. Use the trash barrels.
When field maintenance, such as mowing, is underway, it is considerate and helpful to the maintenance volunteers to not only keep clear of their equipment, but to lend a hand in the moving and relocation of tables.
Avoid, at all times, becoming a nuisance to other park users. Complaints by other park users of our activities may well jeopardize our use of the field.

## Slide 47: Phase 2 Flight Pattern and Basic Orientation
Trim for level flight
L-R Wing Rock Flying Towards Pilot
Level Turns, High Oval Pattern
Climbing Turns (by adding power)
Descending Turns (by reducing power)
Rectangular Pattern
Figure 8’s (introduction)
Phase 2
Page 47

## Slide 48: Trimming
On your first flight, you and your instructor will trim your plane in level flight by adjusting the trim controls until the airplane flies straight hands off
This makes the airplane MUCH easier to fly.
Airplane should be trimmed at about 1/3 to ½ throttle for a relaxed pace, a longer flight, and consistent handling during approach and landing.
Page 48
Phase 2

## Slide 49: Orientation
Left and Right will seem reversed when the airplane is coming toward you
What can you do to learn to deal with this?
    Turn your back to the plane and look over your shoulder
    Wiggle the wings Left and Right with aileron when the plane is flying toward you on the upwind leg
    Talk while you fly, i.e. “I’m now turning LEFT, I’m now rolling RIGHT to stop the turn”, etc.
Page 49
Phase 2
Notes: ORIENTATION.
Maintaining proper orientation is an acquired skill; the result of a great deal of practice. Most beginners struggle to maintain correct orientation.
Ailerons, left or right?
The most troublesome orientation issues involve ailerons particularly when the model is flying towards the pilot, and the roll axis sense appears visually reversed.
This problem seems to occur most frequently when a beginner is flying the normal pattern, takeoff orientation is normal, crosswind is normal, downwind perhaps a little confusing, base leg and final leg are where real orientation problems seem to occur.
There have been several suggestions offered intended to reduce this
confusion. One common suggestion is that the pilot should always hold the transmitter facing the same direction of flight of he model, and look over his shoulder, if necessary, to keep the model in sight. By this means the pilot's fingers move in the "correct" sense.
Another method is perhaps more readily adopted; the pilot talks to himself, issuing what sailors call helm commands. The pilot determines what control input is required, and then issues the command to his own fingers, say, "right aileron". Perhaps the advantage of this method is that it requires the pilot to be mentally ahead of the airplane, visualizing the intended flight path, and intellectually deciding upon the correct helm order, rather that reacting instinctively.
Correct instinctive reaction comes from much practice, and the beginner has not had the benefit of enough practice, so he must concentrate intellectually and plan ahead mentally for each control input.
Coming or Going?
The other situation that often leads to loss of correct orientation is when the model gets too far away, or too high, and becomes simply a silhouette against the sky. "Is it coming towards me or away from me?" is the confused reaction. Quick logical observation is the only solution. Apply gentle aileron to bank the aircraft, if left aileron produces a bank to the left, the aircraft is departing, so keep the bank on through 180 degrees and bring it back. If left aileron produces a bank to the right, the model is returning.
Upright or Inverted?
Upright or inverted? Another potential loss of orientation, quite often leading to a crash. This confusion is more common with low wing or shoulder wing aircraft than with high wing trainers, for obvious reasons. Sharply contrasting color schemes between the upper and underside of the model help, but often, against a bright sky, the model appears only as a black silhouette and color is indistinguishable. With experience this confusion becomes less common as the pilot is more "ahead of the aircraft" mentally.
Takeoff roll confusion.
Many beginners experience confusion and loss of orientation on the takeoff roll, when the aircraft suddenly veers off course, usually to the left. The beginner over-reacts, or reacts wrongly with aileron rather than rudder to correct, and the takeoff becomes a panic. The best and quickest action is to abort the takeoff by chopping the throttle before an accident happens.
The best preventative measure is to advance the throttle slowly at first, allowing time to stabilize the models takeoff heading, rather than slamming the throttle open abruptly at the start of the takeoff roll.

## Slide 50: The Flight Pattern
Page 50
wind
upwind
Cross-wind
Final Approach
downwind
Base
wind
wind
Runway
Phase 2
Notes: Airfield Flying Area
The Marymoor Flying Field (Airfield) Map below shows the permitted Flying Area and the Pylons, Banner and Marker that identify this area to the pilots. This map is shown looking south, which is the view that a flyer will have from the pilot stations along the northerly edge of the runway. To the left and right, a flyer will see a pylon displaying red and white triangles. These two pylons define the safety line which is the northerly edge of the permitted Flying Area. All flying must take place in front of this line (AMA Safety Code). To the left a flyer will see a large banner displaying a red and white checkerboard. This identifies the easterly end of the Flying Area. To the right a flyer will see a tall marker displaying an orange and white checkerboard. This identifies a distance about 100 feet short of the westerly end of the Flying Area (the topography prevented placing the marker at the full distance).
The diagram below details the various components of our field. North is towards the bottom of the page, so that a left to right takeoff on the runway would have your model heading WSW, and a right to left takeoff is in the ENE direction.
The runway orientation is approximately ENE-WSW
PATTERN TERMINOLOGY
Unless wind direction dictates other wise, we conventionally fly a Left Hand pattern at our field. This pattern implies a take off from left to right, a straight climb out, a left turn onto the Crosswind Leg of the pattern, another left turn onto the Downwind Leg of the pattern, another left turn onto the Base Leg of the pattern and a final left turn onto Final for full-stop landing, touch-and-go or fly-by. The pattern should be flown entirely well within the designated Flying Area.
When wind direction requires a Right Hand pattern, take of is from right to left and the same pattern is flown with right turns replacing left turns.
For aerobatics first depart the pattern from the Crosswind to Downwind turn and perform aerobatic maneuvers above and beyond the downwind pattern leg.

## Slide 51: Level Turns
On your first flights, you will work on flying the pattern, with four 90o turns, or two 180o turns
An airplane does NOT turn like a boat or car. Holding the ailerons too long will result in the plane rolling over onto it’s back
To initiate a turn, “poke” in some aileron for less than a second (think “one potato”) to establish a 30-45 degree bank angle, then return the ailerons to neutral.
As soon as the bank angle is established and ailerons are at neutral:
    Ease back on the stick (up elevator) to compensate for altitude loss that will result from the bank angle.
    A good trainer will hold the bank angle, and pulling on the stick will feel like the airplane “carves” a nice, level flight turn.
When the airplane has turned enough, you must stop the turn by applying opposite aileron (with a “one potato” poke) to level the wings. Remember to stop the elevator input too.
Page 51
Phase 2

## Slide 52: Climbing and Descending Turns
Climb by adding some power. The airplane will climb in a controlled way
Descend by reducing power. The airplane will descend without gaining a lot of speed.
Try descending using NO power. Be a glider.
Using only elevator to do climbs and descents will result in big changes to speed, which will in turn cause changes in pitch.
Phase 2
Page 52

## Slide 53: Figure 8’s
Fly in a gentle circle in front of you, focusing on altitude control.
When the airplane is pointed at you, reverse your roll angle to enter the other circle, and so on.
This maneuver improves your skills best if the cross-over is done with the airplane pointed at you
Phase 2
Page 53

## Slide 54: Wind at Marymoor
Usually on nice days the wind is from the right (West)
But we can have crosswinds, coming from behind us (north winds) in fair weather. If the weather is poor or changing to poor, we often have south winds, resulting in crosswind coming toward us.
Check our our personal weather station! (link on the website)
Page 54
North wind
South wind
Phase 2

## Slide 55: Crab Angle
In wind, where the airplane is pointed is not where the airplane is going.
The pilot does not need to hold rudder to maintain a crab angle.
Simply make a turn to fly on the heading that results in the desired track over the ground.
The airplane does not “feel” the wind. It is simply flying in a body of air that is moving with respect to the ground.
Page 55
Heading (where the plane is pointed)
wind
TRACK over Ground (where it’s going)
Crab
Angle
Phase 2

## Slide 56: Flying the Pattern in Wind
Judge the start of your turns. The legs of the pattern last longer or shorter depending on wind direction.
Judge the end of your turns. Turn a little further, or a little less far to anticipate the crab angle for the leg you are flying into
Crosswind and base legs might just become 180 degree turns when the wind is behind the airplane.
While flying the longer upwind or downwind legs, watch to see if the airplane is drifting off course. If so, make a gentle turn to increase or decrease your crab angle.
The same technique applies on final approach
Page 56
Phase 2

## Slide 57: Phase 3 Approach and Landing
Slow flight, stall, and recovery
Trim at approach speed
Instructor demo approach pattern visual cues – left
Instructor demo approach pattern visual cues – right
Stabilized approach
Go-Around – controlled, straight ahead
Flare and touchdown from Left
Flare and touchdown from Right
Approach in crosswind
Dead Stick Landing
Phase 3
Page 57

## Slide 58: Slow Flight
After you’ve mastered flying the pattern at a level altitude, learning how to fly the airplane very slowly will teach you about how pitch and power control speed and altitude
Throttle back, and as the airplane tries to descend, counter that with some up elevator. Now your plane is flying slowly, while you hold elevator to keep altitude
Try flying the pattern slowly. Turns will be tighter so you can use less bank angle. Whenever the plane tries to descend, smoothly add a little power while you hold the elevator. Reduce power smoothly if it tries to climb.
Try this at different throttle settings to see how slow you can go and still maintain control of the airplane
As you get good at this, you may find that using rudder to turn will be more effective, since the ailerons will be less effective due to slower airflow over the wings
Don’t worry, your instructor will make sure you don’t stall, or recover if you do stall.
Page 58
Phase 3

## Slide 59: Stalls
See the Wing Stall explained in Section 4
As you slow further in slow flight by pulling back on the elevator and reducing throttle even more, you can get the angle of attack so high that the wing cannot “hang on” to the air anymore.
The air is meeting the wing at the critical angle of attack.
Lift will reduce and drag will increase
Most trainers will just “mush ahead”, but with poor control because of low airspeed over the control surfaces.
To recover, relax the elevator input and smoothly add power
If one wing stalls first, the airplane will roll abruptly. In this case relax the elevator and input rudder or aileron to level the wings. Check for wing warps after you land.
Page 59
Phase 3

## Slide 60: Centers of Lift and Gravity
Center of gravity must be ahead of the center of lift for the airplane to be stable in pitch (and speed)
Page 60
LIFT
Small
Down
Force
WEIGHT
Center of Lift
(about 25% of chord, or wing width)
Center of
Gravity (CG)
Balance Point
Phase 3

## Slide 61: The CG and Pitch Trim Determine the Speed the Airplane “wants” to Fly
If the airplane is trimmed while flying fast at high throttle, then during approach at low throttle, it will try to fly fast by nosing down
If the airplane is trimmed while flying slower, then it will want to fly at a better speed when on approach
Trim elevator in level flight at 1/3 to ½ throttle to give a relaxed speed:
    Slowing down increases your precious flight time
    Gives you more time to think ahead of the plane, and correct for mistakes
    Produces a comfortable and consistent approach speed
This works well for stable trainers and scale airplanes with cambered airfoils and CG ahead of the center of lift.
CG further aft and symmetrical wing sections on aerobatic airplanes enable them to be trimmed the same at all speeds. Throttle and elevator are used to control speed and altitude on final approach. This is a different technique that experienced flyers are comfortable with.
Page 61
Phase 3

## Slide 62: Getting Ready for Landings - Thinking Ahead of the Plane
Think WHERE you want the plane to be in 10, 20, and 30 seconds from now.
What STATE you want the airplane to be in 10, 20, and 30 seconds from now, i.e. high and fast or low and slow?
Make a plan in your head to get you there
Page 62
Phase 3

## Slide 63: Low Pattern – Getting Ready for Landings
Reduce power a little on late downwind, starting at the same altitude and location every time. Consistency is key here.
Turn to the base leg and level the wings
Make another power reduction. Keep a little daylight between your airplane and the trees.
Turn onto final. Ensure the right landmarks are behind the airplane, so that it approaches the runway on centerline. If you turn too late, just continue the turn until you get to the centerline. Don’t rush or increase the bank angle!
Fly straight at yourself (initially), shallow descent, relaxed speed.
At about 10 feet high, do a missed approach (“Go-around”). Smoothly add power and climb to that same altitude and repeat the process
Page 63
Power Reductions
(for approach from your left)
Phase 3

## Slide 64: Approach Pattern Visual Cues
From the Left
    Base leg just above the tree line
    Turn final just before the gap in the trees where you can see the apartment buildings. This will line you up right over the checkerboard
From the Right:
    Judge the height of the base leg from your experience approaching from the left
    Turn final so that you are above the checkerboard
Phase 3
Page 64

## Slide 65: The Stabilized Approach Key to a Good Landing
Page 65
Make shallow turns to stay on the centerline. (more about crosswinds later)
When landing from the left, you want the plane to be about 1/3 of a tree below the top of the tree line on Final Approach
A stabilized approach is:
Flying in a straight line, wings level, toward the landing zone, parallel to the runway centerline. Your airplane appears above the checkerboard boundary marker.
Descending steadily toward the landing zone – your airplane appears a bit below the top of the trees
Phase 3

## Slide 66: The Stabilized Approach Key to a Good Landing (continued)
If low, add a little power. If high, reduce power
Changing altitude with elevator at this point will de-stabilize the approach, and you will find yourself “hunting” up and down with elevator.
If you trimmed your plane earlier to fly at a relaxed pace (about 1/3 throttle), the airplane will tend to seek a nice steady not-too-fast approach speed, and not much elevator will be needed.
Page 66
Phase 3

## Slide 67: The Missed Approach or Go-Around
You will practice many go-arounds before learning to land
go-arounds also prepare you for takeoff skills
If the approach is un-stabilized, the landing will be lousy too!
Go-around if the approach doesn’t look stable
Go-arounds are free. Bad landings are expensive!
Full scale pilots train the same way.
Page 67
Phase 3

## Slide 68: Executing the Go-Around
During the approach, don’t stare only at the plane. This can cause you to forget where the plane is with respect to the runway while you focus on control.
Quickly glance at the runway end now and then to enhance your awareness of the overall situation.
Know where on the approach (height and position) you will decide to continue to land, or go-around
Then….to go-around,
  Smoothly but promptly add about ½ power. (Since you are slow (at approach speed) DON’T add full power rapidly. A rapid roll to the left might be the result.)
  Fly the airplane – establish a shallow, steady climb – make it go straight on the runway heading
Page 68
Phase 3

## Slide 69: The Touchdown (Finally!!)
If your approach has been stable, continue the glide
Glance at the ground quickly as the plane crosses the runway threshold to orient yourself
Cut the power to idle at the runway threshold, if it is not there already
When the plane is 2-3 feet above the runway, raise the nose slightly, just enough to slow the descent
As the plane slows, it will descend again. Raise the nose a little once more, and wait for it to touch down.
Don’t forget to steer the plane with rudder after touching down!
Page 69
Phase 3

## Slide 70: Recovering from a bad Landing
If you flare too high and the plane is nose up and losing speed, add power and go-around to avoid a stall
If you bounce a little, and the nose is up less than about 15 degrees, just hold it there and wait for the next touchdown
If you bounce a lot – if the nose goes up, add some power and go-around to avoid a stall
Flare and touchdown are difficult if you fly the approach too fast or too slow. This is why we trimmed the elevator for lower speeds earlier.
Page 70
Phase 3

## Slide 71: Approach and Landing in Crosswind
RC flying techniques based on full scale flying are described in articles and online requiring use of rudder and opposite aileron to produce a “forward slip” to counter the crosswind while keeping the fuselage parallel to the runway. For landing on narrow, paved runways with larger planes, these techniques might be necessary – but they are difficult to master.
At Marymoor, we have a huge, wide, grass runway. You still want the discipline to land on the centerline, but an easier technique can be used.
Simply make small turns (with no special use of rudder) during the approach to achieve a crab angle (see slide in Phase 2) that results in the airplane following an imaginary extended runway centerline.
In the flare and touchdown.
    Very close to the ground, the airplane flies into the “boundary layer”, and the wind decreases.
    Grass is tolerant to the airplane landing a little sideways, so don’t worry about a crab angle
    Hold aileron into the wind after touchdown to counter the wind “picking up” the upwind wing
In high winds, flying a somewhat faster approach might help provide needed control, and some margin to stall in case a gust comes from behind and robs your airspeed (known as windshear)
Page 71
Phase 3

## Slide 72: Phase 4 - Takeoff
Straight line on takeoff roll
Controlled rotation and liftoff
Straight ahead climb
Takeoff in crosswind
Phase 4
Page 72

## Slide 73: Instructors Note!
Experience shows we have the most training accidents and damaged airplanes doing takeoffs.
Takeoff is best taught after the student has practiced go-arounds in Phase 3.
If the student over-rotates, or rotates while steering with a rudder input, the instructor may not have enough time to save the plane.
Teaching go-arounds first ensures that the student knows how to smoothly pitch up, and fly a straight-ahead climb in wind
Phase 4
Page 73

## Slide 74: Straight Takeoff Roll
Get lined up. Use the middle of the runway
Hold about 1/3 UP elevator
Smoothly advance power to ½ or more
Steer straight with the rudder – think ahead, and be smooth. The plane may want to turn left due to propeller effects, or it may try to turn into the wind.
If the airplane steers badly, ABORT the takeoff (throttle immediately to idle).
Never hastily pull the airplane into the air.
Never pull into the air with a large rudder input present. The immediate snap roll will ruin your day!
Page 74
Phase 4

## Slide 75: Takeoff Rotation
The airplane will rise when it’s ready, with enough speed, if you are holding some UP elevator. If it doesn’t add a little more gradually.
When the plane lifts off, immediately relax the UP elevator and set a shallow climb to build speed
The airplane may want to turn left. Don’t let it!
    With a crosswind, this can become a downwind turn and stall close to the ground. Force it to fly straight, just like full scale pilots do.
Climb out straight and steady. Build speed. When settled, start your turn to the crosswind leg
Phase 4
Page 75

## Slide 76: Taking off in Wind
Take off into the wind! If others are not, make your callouts clear and loud.
Steer with rudder, but be ready for the plane to weathercock into the wind during the takeoff roll
For crosswinds, hold some aileron into the wind during your takeoff roll.
Be ready for the wind to “pick up” your upwind wing, and correct for it.
After liftoff, ease out the aileron, but gently make a small turn into the wind until you achieve a crab angle so that the airplane flies the runway centerline.
NEVER lift off with a large rudder deflection. This will likely cause an immediate snap roll.
If it doesn’t look good and straight on the ground, abort the takeoff roll.
Page 76
Phase 4

## Slide 77: Phase 5 Advanced Orientation
Figure 8’s (again)
Instructor demonstrate ways to regain orientation
Loop
Immelman Turn
Roll
Phase 5
Page 77

## Slide 78: Figure 8’s
Fly in a gentle circle in front of you, focusing on altitude control.
When the airplane is pointed at you, reverse your roll angle to enter the other circle, and so on.
This maneuver improves your skills best if the cross-over is done with the airplane pointed at you
Phase 5
Page 78

## Slide 79: How to Prevent loss of Orientation, and Regain Orientation
Prevent loss of orientation:
    Think ahead. Plan where you want the airplane to be in 15 seconds.
    NEVER fly directly overhead or behind yourself
    Always remember where you just were a second ago and what you were doing.
    If the plane is getting too small, don’t wait – take action to fly back to you.
    Is it coming or going? Rolled left or right?
    When the silhouette confuses you, making a roll input will help
Page 79
Phase 5

## Slide 80: Loop
Fly straight with wings level and plenty of speed and power
Pitch up smoothly and apply full power
At the top of the loop, pull power back to idle so you don’t get too fast coming down
Continue pitching smoothly
Add the power back in at the bottom
Try to make it
circular, not
egg-shaped
Phase 5
Page 80

## Slide 81: Immelman* Turn
Enter just like the loop
At the top of the loop, neutralize elevator.
Then roll upright
Roll
Upright
* Named for Max Immelman, German WWI ace
Phase 5
Page 81

## Slide 82: Half Cuban Eight Learn to roll first when recovering from a dive
Just like the Immelman, but,
Neutralize elevator a bit later - on a straight 45o down line
Roll upright
Pull out of the dive
Roll
Upright
Pull up
Phase 5
Page 82

## Slide 83: Roll
Level Flight
Nose up
Then, Neutralize Elevator
Full Aileron
Roll all the way around
Phase 5
Page 83

## Slide 84: Recovery From Extreme Attitudes
Later in your lessons you will learn to recover from from very steep climbs or dives, and very steep bank angles, even upside down.
When you are surprised by an extreme attitude, your objective is fix the problem with the smallest loss in altitude, i.e. don’t hit the ground!
Nose high: push elevator nose down to prevent the stall
Nose low: Reduce power to avoid building too much speed, and pull out of the dive with elevator. Pulling too hard or too suddenly can cause a stall.
High bank angle or upside down: Roll to level the wings first, then correct any dive with elevator. Do not pull elevator until the wings are nearly level.
Memorize what Pitch, Roll, and Yaw are so you and you instructor can communicate effectively.
Page 84
Phase 5

## Slide 85: Flying in Gusty Weather
Gust means that the wind speed and/or direction change rapidly
Wind is usually stronger higher up
Gusts may be stronger nearer the ground where the wind whips around obstacles
Try not to fight every gust too hard. It is possible that the next gust will put the plane back in the direction you want.
If your trainer has artificial stabilization modes like “Beginner”, “Intermediate”, and “Advanced”, choosing the Intermediate mode will hellp the airplane fight some of the gusts for you.
Page 85
Phase 5

## Slide 86: Recovery from mishaps
Mental – don’t worry everyone does it! You will learn, and fly again.
Repair – You can fix almost anything if you are determined, and ask for help and advice.
Ask your instructor to teach you dead stick (power lost) landings
If your airplane goes down:
    Put your throttle to idle immediately to avoid damage to the ESC, or to an engine.
    Other pilots at the field are likely to see where it went down. Get someone to go with you. The tall grass and vegetation make finding the plane difficult. Wear long pants. There are nettles out there!
    Take your transmitter with you so you can wiggle the controls and make a little noise. At Marymoor, putting a beeper in your plane is a really good idea.
Page 86
Phase 5
Notes: RECOVERY FROM MISHAPS
EVERY RC FLIER HAS MISHAPS.
With very few exceptions every RC flier has "used up" a few models.
Most of us get through more than one trainer. The "Whoops" moments are more frequent in Ones early days. They become less frequent, but more dramatic later on!
Remember that you are probably not a natural born bird-man, that you will learn more from your mistakes than your successes, and that you have support and counsel in your club and do not become discouraged.
There are, as you know, in any learning experience, periods of rapid growth and also those frustrating slow periods, where we just don't seem to get it. The slow periods are normal, just stick with it, you will get it!
WHEN ACCIDENTS HAPPEN.
We crash our models for a whole gamut of reasons, and we explain them to ourselves by some emotional justification; sometimes valid, sometimes just an excuse, sometimes pure fantasy. We should recognize that most accidents are pilot error, our own fault. Accept accidents as a fact of RC flying life. Accept them with good grace and humor, and above all, learn from them.
There are RC fliers who mount the aft fuselage and tail-plane of their crashed models on plaques on their workshop walls, like hunting trophies. Probably keeps them humble!
Accidents are most frequently the result of the aircraft "getting ahead" of the flier. Keeping mentally ahead of your aircraft is a skill acquired with much practice, like so many other skills involving mental and physical dexterity. The technique requires you to always have a mental image of your intended flight path of the aircraft and the control input required of you to make it happen. If you are waiting to react to the aircraft before you decide upon and input control commands you are already "behind the airplane", and it is in danger of getting away from you.
REPAIR
Crashes damage airplanes, sometimes beyond repair. The extent of the damage, and the feasibility of repair is yours to assess and decide.
Of the wide variety of model types flown by us the electric foamies are least liable to suffer terminal crash damage due to their light weight and flexible structure. Even when damaged their molded foam structure is very often repairable simply by glueing back the damaged components with foam-safe CA or one of the other appropriate adhesives.
ARF models, usually of lightply and balsa construction are more demanding to repair. Many of them are designed and built very lightly, and the quality of their glue joints is frequently dubious. Repairs can, of course, be made, but the repair usually adds weight to the model, so CG and trim might be altered as a consequence. In some cases it may be wise to purchase a replacement component, say a new wing, rather than undertake substantial repairs to a delicate model.
Gas or glow powered models may have areas where oil has soaked into the balsa or lightply structure of the model rendering those portions un-glueable for repair. Iron-on film covering, Monocoat for example, will not stick to oil impregnated wood. Very often, therefore repairs to a damaged firewall and/or tank bay in a model become very difficult unless the model was carefully fuel-proofed initially. Unless such repairs are very carefully and properly made the vibration of an IC engine will make the repair unsafe by loosening glued joints. With all IC powered aircraft it is imperative to fuel proof the engine bay, firewall and the tank bay with epoxy resin before mounting or running the engine.
KIt-built or scratch built models are very often repaired by the original builder, who has the incentive, patience, time and skill to do more extensive or complex repairs than most of us.
In every case, the model should be very carefully checked to ensure that the repairs have not resulted in warps, deformations, misalignment or out-of-balance problems.
UNUSUAL ATTITUDE RECOVERY
Recovery from an unintended unusual attitude always requires time and altitude. For that reason, when attempting aerobatics, or any other exuberant flying, always fly 2 or 3 mistakes high.
The wisdom in that advice is that recovery, particularly for the novice, can be a multi-step sequential process; regain correct orientation, level wings, regain level flight, resume breathing. Each requires deliberate, non-instinctive control input. The process takes time, only seconds, perhaps, but at low altitude the time is not available before ground impact terminates the proceedings, so fly 3 mistakes high!
With experience, corrective action becomes more instinctive, but never fool-proof. Even experienced fliers have their bad days.
EMERGENCIES, DEADSTICKS, ETC.
DEADSTICKS. From time to time all IC powered model aircraft experience an engine stoppage in flight. Electric fliers sometimes have ECU failures, battery failures or exhausted batteries in flight. All these trigger emergency deadstick situations calling for prompt and accurate action to avoid a crash.
The worst situation is loss of power immediately after takeoff. Typically the model is climbing steeply at fairly low speed when power is lost. The model does not have altitude to trade for airspeed and has very little excess airspeed in hand. In either case the immediate action that must be taken is to lower the nose to avoid a stall and preserve minimum airspeed. Simultaneously the decision must be made to either land straight ahead, in the rough, or to do a 180 degree turn and land downwind on the runway.
The straight ahead landing is the less challenging option, requiring generally the avoidance of trees, rocks, brambles, etc and to settle as gently as possible into the most hospitable terrain available. Long grass is preferred!
The 180 degree turn option is fraught with hazard. The model must have adequate energy to carry it through the turn, either in the form of altitude or airspeed. The model must maintain airspeed through the turn by trading altitude for airspeed. Typically the model is flown through a steeply banked, tight, descending turn to a downwind heading. The pilot will be tempted to raise the nose trying to stretch the glide to reach the runway. A stall is very likely, and the consequent crash.
For light electric foamies this will not be too dramatic or damaging but also infrequent an accident, for such models do not often lose power on takeoff. IC powered models do suffer this condition, fairly frequently.
In either case, as soon as power is lost, the flier should call out loudly, "Deadstick, deadstick, deadstick" as a warning to others flying, and a request to clear the immediate area.
In general, and in common with full-size aviation, good advice is to choose the straight ahead option.
IN FLIGHT EMERGENCIES. Most common such an emergency is loss of power. This is a real problem if the loss of power occurs at low altitude downwind on the landing strip. A landing in the rough is probable. Just as in the takeoff emergency discussed above, announce your "Deadstick" loud and clear, lower the nose, head for the runway. Avoid trying to stretch the glide by raising the nose and if an off-runway landing is unavoidable, choose the best terrain for the landing.
In any emergency situation, make your intentions very clear, immediately, to the other fliers on the flightline so that they clear the area for you.

## Slide 87: Skills to Refine before your Solo Check Flight
Thinking ahead of the plane
Awareness of boundaries
Smooth flying for all skills
The stabilized approach – Key to good landings
Approach and landings from both directions
Smooth Go-Around with control of your heading
Touch down where you planned to
Flying in Wind
Figure 8’s with good altitude control
Simple aerobatics and recovery from extreme attitudes
Page 87
Phase 5

## Slide 88: Proficiency Check Flight
You will fly multiple instructors during training. When you are ready to fly solo, you will fly with two instructors for two flights. These flights will be done without a buddy box.
In each flight you will be required to:
    Demonstrate a before start check of your model
    Taxi
    Demonstrate a pre-takeoff check
    Make appropriate callouts
    Takeoff and climb out straight ahead
    Fly a rectangular pattern in level flight
    Do a stall, and recovery with minimum loss of altitude
    Fly a figure eight showing good altitude control
    Fly a stabilized approach and a missed approach from both left and right
    Fly an approach into the wind, and land
Phase 5

## Slide 89: MAR/C Proficiency Check Quiz Page 1 of 2
Name the national organization that guides and self-regulates flying models.
Name the federal agency with legal authority that regulates flying models.
What information should you to have marked inside or on your model?
Under the FAA sUAS (Small Unmanned Aircraft System) program, what altitude should you not exceed?
How far must you be from an airport when you fly?
When performing a pre-flight (before start) inspection what are you going to inspect?
In addition to the pre-flight (before start) check, what is your before-takeoff checklist?
How many pilots are allowed to fly at any one time at the Marymoor Field?
Are you allowed to fly behind the pilot stations with your model?
Phase 5

## Slide 90
Can you explain the markers that define the Marymoor flying boundaries?
What park areas are just outside our boundaries? Why must we stay inside the boundaries?
When flying, what callouts are you expected to make?
When are you allowed to fly a low pass over the landing area?
Before plugging in a battery on an electrically powered aircraft: a. The throttle lever on the transmitter should be where? b. The T_ _ _ _ _ _ _ C_ _ switch on the transmitter (if available) should be set to I n _ _ _ _ _ c. The switch on the airplane for the ESC (if available) should be _ _ _ , or the safety plug (if installed) should be un – p l _ _ _ _ _.
a. Before starting a gas or glow powered aircraft, it must be R e _ _ _ _ _ _ e d. b. An electric S_ _ _ _ _ _ should be used to start the engine. c. If starting by hand, a chicken S t _ _ _ must be used to start the engine.
Lithium polymer batteries can be a _ _ _ _ hazard. They should be charged and stored in a _ _ _ _ - proof container, such as a _____________. They should be charged only by LiPo capable chargers at the correct charge _ _ _ _ for that battery.
What airplanes must pass a 90 db noise measurement?
Phase 5
MAR/C Proficiency Check Quiz Page 2 of 2

## Slide 91: Section 6
Radios
and Electronic Speed Controls
Page 91

## Slide 92: Radio Antennas
Transmitter - Correct Antenna Orientation
  The signal from the SIDE of the antenna is MUCH STRONGER. “Pointing” the antenna at the airplane sends the WEAKEST signal.
  For older 72 MHZ radios extend the transmitter antenna to it’s full length before flying or range testing the aircraft.
Receiver – Correct Antenna Installation
  The 2.4 Ghz antenna needs to be placed inside the model away from moving parts and wires
  2.4 Ghz antennae MUST be oriented 90 perpendicular to each other, and as far apart as wiring allows. Read your radio manual.
  An older 72 Mhz antenna will be a long wire that will run the length of the model. Do not cut the length or tie in a large loop at the back of the model.
Above all – READ your radio manual instructions
Page 92
Strong
Weak
Long antenna taped in
Place lengthwise
Short Antenna taped in place
Example
Notes: Link http://rcvehicles.about.com/od/frequency/a/antennas.htm
RC Transmitter Antennas
Fully extend the antenna before operating your radio controlled vehicle. Not fully extending the antenna on the controller can affect your range and ability to control the RC. If your RC is behaving erratically or isn't responding to your controls, it might simply be because your antenna is not fully extended.
Whenyou put down your controller (such as during a pitstop) retract or collapse the antenna so that it doesn't get in your way or become damaged. Avoid pulling forcefully on a telescoping antenna or retracting/collapsing it by pushing down from the top. Retract it by lightly grasping it and sliding it down a section or two at a time. Even though the telescoping metal antennas appear fairly sturdy, even they will bend and break.
RC Receiver Antennas
To keep long receiver antenna wires from dragging on the ground and getting caught in the wheels of your RC, the antenna is often placed in a piece of flexible (but somewhat rigid) piece of tubing. The antenna sticks up above the RC but remains flexible so it doesn't break easily in a crash or rollover.
Pictures of Flexible Antennas
Receiver Antenna Hanging Out of Antenna Tube
Why RCs Need Flexible Antennas
Installing the Receiver Antenna To make it easier to thread the antenna wire through tubing, you could lubricate it with a touch of oil -- but oil can become sticky and does attract dust and dirt. An alternative lubricant is talcum powder. Put a little in your hand, hold the antenna and draw it through your hand to coat it. You could try sucking the antenna through the tube. Or, suck a piece of thread or dental floss through the tube, tie it to the antenna, then pull on the thread or floss pulling the antenna through the tubing.
To keep the antenna from sliding back through the tube, tie a knot in the end (only works with very narrow tubing) or add a rubber or plastic antenna cap on the end.
Pictures of Receiver Antenna Preparation
Threading Antenna Thru Tube
Adding an Antenna Cap
Don't Cut the Antenna Cutting the antenna wire on your RC can increase the chance of interference while trying to operate the RC causing glitches. Don't cut the antenna wire. To keep the antenna from dragging, you can thread it through an antenna tube -- if you don't have an antenna tube you can try soda straws, hollow coffee stirrers, or other semi-rigid plastic material.
Some radios may operate fine with shorter antennas. Cut the receiver antenna only if the manufacturer says it is OK. Be sure not to cut it any shorter than the manufacturer recommends.
If the long antenna is really bugging you, you can try securing the excess wire inside the vehicle. Be careful not to coil or bunch it too tightly as this can cause glitches. You can attach the excess antenna to the inside of the body, but this can make it difficult to remove the body to get at the internal parts. Even better, after running the antenna through the antenna tube, wrap the excess around the outside of the tube in a spiral. Don't wrap it too loosely but do space it out so that it isn't all bunched up in one spot. Use a little piece of electrical tape to secure the loose end to the tube. Add an antenna cap to further secure it.
Make sure that your receiver antenna is not touching any metal parts inside the RC -- this can cause glitches and erratic behaviour too. You can wrap it somewhat loosely around a piece of cardboard and attach it to the receiver or the body. Threading the antenna through a piece of flexible tubing -- such as fuel tubing -- or wrapping it in a strip of electrical tape will help protect it from damage and keep it from touching metal. As much as possible, try to keep the receiver antenna fully-extended and not wrapped or doubled-up.

## Slide 93: Setting the controls for You
Stick Forces
Dual Rates
“Expo”
Aileron to Rudder mix
Throttle cut
Page 93

## Slide 94: Stick Forces
Stick forces on many transmitters are adjustable. Read your manual
Increasing forces can help a lot with over-controlling early in the learning process
One professional RC flight school even puts custom, stronger springs in their transmitters
Control forces and Dual Rates are the first things to adjust if your instructor feels you are over-controlling.
Page 94

## Slide 95: Dual Rates
Sets up switches on the transmitter so you can select more or less control throw for Aileron, Elevator, and Rudder
Generally start with the control throws recommended for your airplane
For any first flight, it’s a good idea to have options. Take off in low rates to begin with
Rates too high, or too low can cause problems
Page 95
Even many simple transmittersmay have a dual rate switch
Example of a programmable “computer” radio screen showing dual rate setup.

## Slide 96: “Expo” (Exponential)
Expo can “soften” the response around neutral and help prevent over-controlling
Mostly used for high performance 3D airplanes that would be difficult to control around neutral because of their very high control throws (rates)
Can be used as you prefer for a trainer (not too much though – probably 30% or less
Not available on “simple” transmitters
Page 96
Expo is NOT the first choice to make an airplane handle nicer – adjust the throws (rates) first
Too much Expo can cause difficult handling
          Expo the wrong way can be disastrous!
      Good” expo is a positive number on Spektrum and JR
    Good” expo is a negative number for Futaba! (Read your Manual to be sure)
Compare this curve
to the straight line one the
previous slide

## Slide 97: Aileron-to-Rudder Mix
Most radios (not the cheapest ones) can do this
Causes rudder to move also when the right stick commands ailerons
Setting the “gain” at 50%, so that rudder moves about half way when the ailerons are fully deflected, is about right for most trainers.
Gives most trainers a smoother and more predictable response to a roll (aileron) command from the pilot.
Make SURE that rudder moves Right for a Right aileron command (and similar for Left)
SHOW THIS to your instructor before you fly
You can put the mix on a switch so that you can take off normally, and then try the mix for the first time when at a safe altitude. And turn the mix off again if you don’t like it.
Page 97

## Slide 98: Propeller Safety Features
Throttle Cut function enables a switch to tell the transmitter to send zero (or less) throttle no matter where the throttle stick is. Read the manual for your transmitter to program it.
Page 98
Use Throttle Cut function if your transmitter has it. Assign the function to a switch that you won’t bump in flight
Use an ESC switch, if your ESC has one
Or install a safety plug on the airplane like this one:
Used to stop “glow” or gas engines
Glow and Gas Engines
Electric Power

## Slide 99: The Electronic Speed Controller (ESC)
The ESC takes commands from your radio receiver, and tells the electric motor how fast to run by turning the power on and off very fast.
It also powers your radio receiver, (larger planes often use a BEC and separate battery)
If your propeller is ever blocked for any reason, like if the airplane noses over or runs into tall grass, immediately pull your throttle stick to idle to avoid damaging the ESC
ESC’s usually have safety features to prevent them coming ON when plugged in – but don’t rely on that alone. Make sure your stick is at idle before plugging in
    ALWAYS read the instructions for your ESC. There are differences between brands!
Page 99

## Slide 100: Battery Power for the Receiver and Servos
Power to the receiver (and the servos) can come from either:
    The ESC on an electric airplane, if that ESC has a BEC (Battery Eliminator Circuit) or
    A separate battery, for gas and glow airplanes
A separate battery for radio is sometimes also used on larger electric airplanes, to ensure control of the airplane even if the motor battery dies or if the ESC fails
Page 100

## Slide 101: Electric Motor and Prop
The right prop is determined by the airplane size, motor size and type, battery, and ESC.
The wrong prop diameter or pitch can cause excessive electrical current and damage the ESC or battery
Use eCalc or other online tools, or a current meter to determine the right prop. If you don’t know for your airplane, don’t guess.
Page 101

## Slide 102: Section 7
Choosing, and getting help with your next airplane
Page 102

## Slide 103: Get ready for your Next Airplane
Fly with your trainer until you feel you have mastered it
Pay special attention to stabilized approaches
Get proficient with simple aerobatics
Page 103

## Slide 104: Choosing your 2nd Airplane
Ask other pilots for their advice
Choose a low-wing with some dihedral, or a high wing with less dihedral than your trainer
Choose a slightly faster and more aerobatic airplane
Park-zone T-28 is a good candidate
Feel free to try a tailwheel airplane. Steering will be more challenging on takeoff, but the landing gear will be more robust.
Avoid retractable landing gear. It is more fragile and more expensive. At this stage, you can still expect hard landings.
3D aerobatic planes, fighters, and ducted fans are good choices for that 3rd or 4th airplane
Page 104

## Slide 105: Get help before you fly the next new airplane
Ask other pilots to look over the plane before first flight
Consider having a more experienced pilot do the first flight to get the plane trimmed properly
Page 105

## Slide 106: Web resources
Aerodynamics
Building technique (you-tube)
How to fix an ARF (look for you-tube help)
YouTubes of stalls, downwind turns, classic stall-spin turning to final
Page 106

## Slide 107: Links
AMA Safety Code
Know before you fly
AMA
Page 107

## Slide 108: Future topics
Building from kits, plans, or scratch
Assembling ARF’s
Hobby shop sessions - covering, hinging, radio installation, etc.
Preflight, range checks
First flight assistance, trimming
In what ways will your second and third airplane fly differently
What you should and shouldn’t choose
Wing Loading — what is it and why should I care
Cubic loading, Reynolds number, other advanced topics
Basic programming for a better flying airplane
About wings and airfoils - different uses and characteristics
Pushrods and control linkage geometry
Page 108