## Slide 1: Aero 101 for R/C Pilots Part 2
Brian D. Kelly
February 2018

## Slide 2: Common Questions from RC Pilots
Part 1 (June 2017)
Before takeoff
  Will this plane be stable?
Takeoff
  How does the prop affect the airplane?
  Do I need right thrust?
  Wind
  Is the “downwind turn” a myth?
Cruise
  How to fine-tune the cg
  Do I need down thrust?
General Handling
  Plane snaps out of a tight turn
  Does dihedral help or hinder me?
  Won’t respond to aileron when slow
  Unstable or too sensitive?
Part 2 (Feb 2018)
Approach
  How can I slow down safely?
  Should I re-trim for approach?
  Use elevator or thrust?
  What will flaps do?
  Handling Crosswinds
Judge what a new plane will be like
  Wing Loading and stall speed
  Power loading
  Aspect Ratio
  Servo size
Part 3
  How can I use my computer transmitter to make the airplane more enjoyable or easier to fly?

## Slide 3: How slow can I go on approach?
Full Scale planes use 1.3 x Stall Speed
  enough speed to avoid stall while turning onto final approach and deal with some turbulence and pilot lack of precision
Stall Speed:
  Wing (Airfoil, Wing Area, Planform, Flaps)
  Weight
  Load Factor (G’s) (Bank Angle)

## Slide 4: Problem: No Airspeed Indicator
We eyeball ground speed and angle of attack
We might hold the nose up a little to cause a lower glide speed
Requires skill, and not every approach is at the same speed
a
q
g
flight path
pitch
a angle of attack

## Slide 5: How do YOU control speed on the approach?
Just throttle back and glide
Hold some UP elevator
Re-trim the airplane to add some UP elevator (like full scale airplanes)
Some combination
Not sure – sub-conscious skill !!
The best technique depends on CG, or balance point
Wait, what?

## Slide 6: Centers of Lift and Gravity Determine Pitch and Speed Stability
Small
Down
Force
LIFT
Center of Lift
about 25% of Mean Aerodynamic Chord (MAC)
Center of
Gravity (CG)
Balance Point
WEIGHT
About 10-20% MAC for stability
Can be aft of center of lift for aerobatics
Too far aft, and the “neutral point is reached (truly unstable)

## Slide 7: Trimmed Flight for Stable Airplane
W
d
(Tail down-force)
L
High Airspeed
W
d
(Tail down-force)
Low Airspeed
L
At low airspeed,
more up elevator
is needed to trim

## Slide 8: Response to Speed Changes
Trim for mid to low power
Fly high and level
Nose down about 45o
Hands off controls
Let airplane accelerate
Observe pitch
Another way:
http://www.flyrc.com/aerobatic-trimming/
Neutral
(for aerobatics)
Nose Heavy plane
pitches UP!
“speed stable”
Tail Heavy plane pitches DOWN!
Not speed stable
Difficult to fly on approach
Trim speed
Speed increases

## Slide 9: Should I Re-Trim for the Approach?
If your plane is speed-stable (a little nose heavy), and trimmed for “cruise”
  Hold UP elevator to glide slower on approach
    (Down-thrust reduces the need for this)
  OR re-trim for approach speed (put in some up-trim)
  OR program transmitter to put in some UP elevator on a switch
  OR program elevator with flaps to achieve low trimmed speed
If your plane is neutrally stable (dive test)
  no re-trimming needed any time
  somewhat more difficult to fly approaches consistently, but “expert” pilots have no trouble

## Slide 10: How to find the trim setting for Approach Speed
Get comfortable practicing stalls at high altitude
Cruise slowly at about 1/3 power
Trim the plane for hands-off level flight (elevator trim)
Glide at zero power, no elevator input – trim again if needed for nice glide at approach speed
Do 45o bank turns to ensure stall margin
Pull into a stall during the turn to “feel” stall margin
Do approaches without holding elevator to see what speed the glide is
Airplane should seek and hold a reasonable speed during the approach without having to hold elevator
Be ready for large pitch-up during a go-around

## Slide 11: Should I Control Altitude with Elevator or Thrust on Approach?
If speed is high, elevator works for altitude control
If too slow, power required increases when pitch up - “back side of power curve”
Normal approach is slow, but not “back side” (unless very low aspect ratio)
Power Required
Speed
“back side”
Normal

## Slide 12: Answer?
On approach, make small altitude corrections
  -- with elevator if you are fast (but you shouldn’t be)
  -- with power if you are slow
Always strive for a “stabilized approach” – nice and straight with small corrections
Ideally, trim for a hands-off approach, and make small altitude corrections with power

## Slide 13: What will happen with Flaps?
Max lift coefficient, Clmax increases
Stall speed decreases
Drag increases
  A little power might be needed
Airplane may pitch (usually up)
Approach will be more nose down
Use same technique to trim for approach speed
  Use flap>elevator correction to trim for approach speed when flaps are down

## Slide 14: Wind on the Approach
Check the sock or feel the wind on your neck
Hold wings level on approach, and watch for drift
If drift, make a small turn, level wings, and assess again
Holding a crab angle is simply holding a heading with wings level – no need to hold rudder or aileron
Holding rudder will introduce unwanted roll in trainers
Airspeed
Ground speed
Wind

## Slide 15: Wind at touchdown
Full scale technique is to lower the upwind wing to counter crosswind, and align fuselage to the runway with the rudder a bit before touchdown.
RC pilots of large airplanes on paved runways might use this technique – not easy!
Luckily, less wind close to the ground
With a grass field, landing in a crab is no problem

## Slide 16: Judging what a new plane will be like
Wing Loading, airfoil, stall speed
Wing “Cubic Loading”
Power Loading
Aspect Ratio
Servo torque requirements

## Slide 17: Wing Loading
Ounces of airplane weight per square foot of wing area
Wing loading = Weight (oz.) / Wing area (square feet)
Higher wing loading = higher stall speed
Low: 5-15
  Trainers, light foamies
Medium: 15-30
  Sport planes, some 3D planes
High: 40 - 50 oz./ft2
  Large Warbirds
  Mr. Mulligan

## Slide 18
Cl max (Stall) low Rn
Cl max (Stall) high Rn
From airfoiltools.com
Semi-symmetrical NACA 2412 at Rn= 50,000, 200,000, and 500,000
Cl
a
Stall occurs at Maximum Lift Coefficient
We fly at low Reynolds numbers Clmax around 1.2 for typical airfoils A little more for high camber and flat bottom airfoils, about 1.4
CLmax for the whole wing is lower due to tip effects, maybe 20-30%

## Slide 19: Lift Coefficient and Dynamic Pressure
Dynamic Pressure (aka “flat plate drag)
    q is dynamic pressure in pounds per square foot
    r (Greek letter rho) is density of air. 0.002378 slugs/ft3 at sea level
    V is velocity, or speed, in feet per second
    q = ½ r V2
V
D
S
Flat Plate
Drag = Cd q S
Cd is Coefficient of Drag
S is the reference area
  (usually frontal area)
Lift = CL q S
CL is Coefficient of Lift
S is the reference area,
(usually wing area)

## Slide 20: How to Calculate Stall Speed
L = CL q S
L = CL ½ r V2 S Lift = Weight
V = √2 W / (CL r S)
Vstall feet per sec = √2 W / (CLmax r S)
= 0.002378 slugs/ft3
W = weight in pounds
S = Wing area in square feet
V = speed in ft/sec
Ft2 = in2 / 144
Vmph = Vft/sec x 0.68
Get Clmax for airfoil from airfoiltools.com – use data for low Reynolds number
Crudely estimate CLmax for the wing by reducing Clmax for airfoil by 20-30%
  More reduction for low Aspect Ratio, e.g. many jets
  Less reduction for higher Aspect Ratio

## Slide 21: Estimate Stall Speed from Wing Loading
Chart: Clmax for airfoil = 1.2 CLmax = 1.0 assumed for Wing
| 4.0 | 8.0 | 16.0 | 32.0 | 48.0 | 64.0
 | 9.0271 | 12.7663 | 18.0542 | 25.5325 | 31.2708 | 36.1084
This estimate works for conventional configuration airplanes – not for delta planforms and scale jets

## Slide 22: Wing Cube Loading
Two airplanes of different size will seem more similar in flight if they have the same WCL.
Accounts for larger airplanes seeming slower and having proportionally lower stall speeds
Works for similar configurations and similar power loading
See a thorough explanation by Francis Reynolds at:
      http://www.theampeer.org/CWL/reynolds.htm
WCL = oz. / (wing sq. feet)1.5

## Slide 23: Wing Loading, Cubic Loading, and Stall Speed
Chart: CLmax = 1.0 assumed for the Wing
| 6.582857142857143 | 7.68 | 9.216 | 11.52 | 12.8 | 14.4 | 16.45714285714286 | 19.2 | 23.04 | 28.8 | 38.4 | 57.6
Stall Speed mph | 12.6858 | 13.7022 | 15.01 | 16.7817 | 17.6894 | 18.7625 | 20.0579 | 21.665 | 23.7329 | 26.5342 | 30.639 | 37.525
Cubic Loading | 1.3352 | 1.6826 | 2.2118 | 3.0911 | 3.6204 | 4.32 | 5.278 | 6.6511 | 8.7431 | 12.2188 | 18.8121 | 34.56

## Slide 24: Power Loading
Airplane Type | Watts per pound | Horsepower per pound | Cu. Inches per pound | Cubic centimeters per pound
Slow Flyer | 50 | .07 | .04 | .67
Powered glider | 50-80 | .07 - .11 | .05 | .87
Sport Flying, aerobatics, warbirds | 80-120 | .11 - .16 | .08 | 1.34
Pattern | 120-180 | .16 - .24 | .12 | 2.01
Faster jets, 3D | 180-200+ | .24 - .27 + | .16 | 2.55
Based on 10cc/hp for OS GT60 2-stroke gas engine
Results differ for 4-stroke, and multiple cylinders

## Slide 25
Aspect Ratio
S (area)
AR = b/c for a rectangular wing
Or..
AR = b2/S for any planform
b (span)
c (chord)

## Slide 26: Aspect Ratio

## Slide 27: Low AR planes fly approach on “back-side” of power curve
Much drag at approach speeds
Thrust MUST be used to control altitude
UP elevator will increase drag so much that speed will drop and airplane will descend!

## Slide 28: Lift and Drag for a Total Airplane
Total Drag = Parasite Drag + Induced Drag
    CD = Cdp + Cdi
Parasite Drag, Cdp is skin friction + pressure drag (aka form drag)
    Measured when Lift = 0
Induced Drag, Cdi , aka “Drag due to lift”
    Cdi = CL2 / (p e AR)
        e is an efficiency factor for the wing, how close it is to the “ideal” elliptical lift distribution
        AR is Aspect Ratio = Span2 / Area
At the speed for best L/D, Induced Drag is equal to parasite drag!

## Slide 29
Increases with V2
Increases with 1/ V2

## Slide 30: Effect of Low Aspect Ratio
Induced Drag (drag due to lift) becomes dominant quickly at low speeds
Any effort to increase altitude with elevator reduces speed and increases drag immediately – and then altitude drops!
Altitude must be controlled with thrust
Low AR
Higher AR
Power Required
Speed
“back side”
Normal

## Slide 31: How Big Should the Servo Be?
Crude Estimate of Hinge Moment:
Assumptions:
  Uniform pressure distribution
  Pressure is dynamic pressure q = ½ r V2 (pounds per sq. foot)
Hinge moment = Force x lever arm
= q x (sq in of surface) x C/2 x 16/144
= 0.5 x 0.002378 x (speed in ft/sec)2 x C/2 x 16/144
= torque, oz - inches
C
(inches)
Average Chord
V
ft/sec
Ft/Sec = mph x 1.47