## Slide 1: Aero 101 for R/C Pilots Part 3: Programming your Transmitter to make the Airplane Easier and More Enjoyable to Fly
Brian D. Kelly (BK1) and Brian L. Kelly (BK2)
November 15, 2018

## Slide 2: Common Questions from RC Pilots
Part 1 (June 2017)
Before takeoff
  Will this plane be stable?
Takeoff
  How does the prop affect the airplane?
  Do I need right thrust?
  Wind
  Is the “downwind turn” a myth?
Cruise
  How to fine-tune the cg
  Do I need down thrust?
General Handling
  Plane snaps out of a tight turn
  Does dihedral help or hinder me?
  Won’t respond to aileron when slow
  Unstable or too sensitive?
Part 2 (Feb 2018)
Approach
  How can I slow down safely?
  Should I re-trim for approach?
  Use elevator or thrust?
  What will flaps do?
Judge what a new plane will be like
  Wing Loading and stall speed
  Power loading
  Aspect Ratio
  Servo size
Part 3
  Programming your Transmitter to make the Airplane Easier and More Enjoyable to Fly

## Slide 3: Better Handling Qualities and More Fun
End points, rates and expo
Unstable or too sensitive?
Using mixes
Aileron to rudder mix
Knife-edge mix
Flap-elevator functions
Elevator to flap mix
Ailerons as Flaperons
Flaps as Flaperons
Reflexed ailerons
Crow (Airbrake)
Throttle to Elevator mix
Flight Modes (Conditions)
Throttle cut on a knob
Engine ignition or motor kill switches
Differential thrust for Multi-engine
Logical switches
A VTOL concept

## Slide 4
This presentation uses
Spektrum DX18 & Futaba T14SG
But general principles apply to any radio

## Slide 5: Be Careful!!
When trying any new mix, rate, or Expo, you are a TEST PILOT.
Do a thorough control check before taking off
Enable new functions with a switch
Turn them on for the first time at a safe altitude and moderate speed
Evaluate flight characteristics (e.g. stalls, steep turns, etc.) at a safe altitude

## Slide 6: Control Throw & Dual Rates
Higher slope means more sensitive, i.e. more surface motion for same stick motion
Plane may be hard to control if rate (throw) is too high
Pilot might mistakenly believe the airplane is “unstable”
Low Rate, less throw
High rate, more throw
Stick Movement
Surface Movement

## Slide 7: EXPO is a way to get lower slope around neutral while keeping high control surface throw
Positive % is “good” expo on Spektrum
Negative % is “good” expo on Futaba
0-30% typical for sport planes
50% or more often used for 3D planes
No expo
More expo
Stick Movement
Surface Movement
Less sensitive around neutral.
More sensitive at high stick positions.
Too Much expo can cause control to change suddenly above half stick.
For example, too much expo could make flaring for landing more difficult

## Slide 8: Spektrum
Dual Rates
Dual Rates and Expo

## Slide 9: Futaba
Dual Rates
Dual Rates and Expo

## Slide 10: “My plane is hard to control in Roll.” Is it Unstable or Too Sensitive?
Most likely “too sensitive”
  Reduce throws
  Try EXPO
  Or try an airplane with high wing or more dihedral
Roll:
  Not likely to be “unstable” in roll unless wing has anhedral or forward sweep. (F-104 is an exception. See Aero 101 part 2.)
Yaw:
  Not likely to be “unstable” in yaw unless fin and rudder way too small, tail too short, or CG much too far aft.

## Slide 11: Review: Pitch Stability Dive Test
Trim for mid to low power
Fly high and level
Nose down about 45o
Hands off controls
Let airplane accelerate
Observe pitch
Another way:
http://www.flyrc.com/aerobatic-trimming/
Neutral
(for aerobatics)
Nose Heavy plane
pitches UP!
“speed stable”
Tail Heavy plane pitches DOWN!
Not speed stable
Difficult to fly on approach
Trim speed
Speed increases

## Slide 12: “My plane is hard to control in Pitch.” Is it Unstable or Too Sensitive?
If not “speed stable”, move CG forward
If “speed stable”, then elevator throw is too large, horizontal too small, and/or tail too short
Solutions:
  First, reduce elevator throw (experiment with dual rates)
  Second, try EXPO…. Unless it’s a 3D plane, then go for expo first
    Remember, “good” expo is a negative number for Futaba radios
  Last, try adding horizontal tail area or tail length

## Slide 13: Using Mixes
Mix: Input to one channel also affects another
  Aileron > Rudder causes Aileron and Rudder to move when the Aileron stick is moved
A mix can also cause a switch or knob to affect another channel
  Knob > Throttle can be a throttle kill function using a knob instead of a switch

## Slide 14: Switches to Control Mixes
Mixes can be ON all the time or be turned ON or OFF with a switch
One switch (like a Flap switch) can be used to control many mixes
    Flaps
    Drooped or reflexed ailerons
    Aileron>Rudder
Multiple mixes can be used to do things like differential throttles on a multi-engine airplane
Mixes can be a straight percentage, or be programmed to work on a curve

## Slide 15: Aileron to Rudder Mix
About 50% works well with trainers.
  Full aileron gives 50% rudder
Smoother entry and exit for turns
Improves poor roll effectiveness at low speeds
A roll becomes a non-axial barrel roll with mix ON
For airplanes that do not naturally do an axial roll, a slight “negative” mix, i.e. right aileron causing slight left rudder, can make rolls more axial

## Slide 16: Aileron-Rudder Mix - Spektrum

## Slide 17: Aileron Rudder Mix, only when flaps are down - Spektrum
B is also the Flap switch, so in this example, the mix only works when flaps are down, positions 0 and 1
Current switch position
Mix active switch positions, in black

## Slide 18: Aileron-Rudder Mix - Futaba
Actual Mix Value from Fine Tuning
Programmed
Mix Value
Fine Tuning Knob Authority

## Slide 19: Knife-Edge Mixes
Used to counter rolling and pitching tendencies with large rudder input
RUD > AIL
RUD > ELE

## Slide 20: Knife Edge Mix - Spektrum
One mix pick does both
RUD > AIL
RUD > ELE
Typically use small corrections
Different corrections usually needed for left and right rudder inputs

## Slide 21: Knife Edge Mix - Futaba
-20 Elevator throw
at -100 Rudder throw

## Slide 22: Flap to Elevator Mix
Gives elevator to cancel out unwanted pitch when flaps are down
Flaps down usually results in pitch up
5 to 10 percent elevator down usually works
Can be used with or without flaps to bias the elevator to give a trim state resulting in slower speed for approach and landing

## Slide 23: Flap to Elevator - Spektrum

## Slide 24: Flap to Elevator - Futaba
Indicates Flap switch or slider position

## Slide 25: Elevator to Flap Mix
Flaps DOWN with UP elevator makes for very sharp pitch maneuvers or tight turns
Increases lift instantly, even before airplane pitches
Old trick from control-line stunt airplanes
Feels like a more sensitive elevator

## Slide 26: Elevator to Flap Spektrum

## Slide 27: Elevator to Flap Futaba

## Slide 28: “Strip” Ailerons as Flaperons
For full span “strip ailerons”
Two-servo, two-aileron wing (without separate flaps)
Both ailerons can be commanded to “droop”, making a kind of full-span flap
Not recommended if ailerons are mostly outboard due to danger of tip stall

## Slide 29: Ailerons as Flaperons - Spektrum
In SYSTEM SETUP menu, under Aircraft Type, select FLAPERONS as a WING TYPE
Set up flaperon throw and elevator compensation in Flap System menu

## Slide 30: Ailerons as Flaperons - Futaba
Program Mix. Can be proportional on a slider
Right Slider > Aileron

## Slide 31: Flaps as Flaperons
For a 2-aileron, 2-flap wing
Flaps move with ailerons to increase roll rate
Caution: Can actually reduce roll rate if used with large flap angles
  Increased flap deflection may result in more flow separation, thus reducing lift and increasing drag on one side

## Slide 32: Flaps as Flaperons - Spektrum
Enabled when WING TYPE is 2 ailerons and 2 flaps
Flaps will move either together or opposite depending on whether LFL or RFL is chosen
This example turns Flaperon function ON only when flaps are up (Switch B = 2)

## Slide 33: Flaps as Flaperons - Futaba
Use canned mix: AIL > CMBFLP

## Slide 34: Reflexed or Drooped Ailerons
Both Ailerons reflexed upward can reduce tip stall
Drooped Ailerons can reduce stall speed when used in conjunction with flaps, but with increased risk of tip stall.
Typically uses during approach or takeoff
Can activate with flap switch positions

## Slide 35: Reflexed or Drooped Ailerons - Spektrum
Mix FLAP > LAL or RAL
Ailerons will move either together or opposite depending on whether LAL or RAL is chosen
May assign switch to flap positions. In this example, only at full flaps, Flight Mode switch = 1
Curve mix shown gives movement in one direction only, but can also be done with anormal mix

## Slide 36: Reflexed or Drooped Ailerons - Futaba
Can use AIRBRAKE, but not proportional
Or use FLP > AIL

## Slide 37: Crow, or Butterfly
Use a switch, knob, or slider to move ailerons up and flaps down simultaneously to increase drag
Often used on competition RC sailplanes with large throws to greatly increase drag and enable steep approaches to spot landings
Found in sailplane menus
… or separate program mixes
    Aileron part: Same as reflexed ailerons, but much more travel

## Slide 38: Crow using programmable mix - Spektrum
Can use Camber Presets in Spektrum if the Model Type is selected as “Sailplane”
Or use programmable mixes for airplanes
Ailerons must have large throw without binding to allow for the large reflex plus normal aileron travel

## Slide 39: Crow - Spektrum
Mix 8 reflexes ailerons up whenever button -I- is pressed
Mix 9 lowers flaps whenever button -I- is pressed
Mix 9 only works if flaps are up (switch B=2) so that no additional flaps are commanded if flaps are already down

## Slide 40: Crow - Futaba
Could use AIRBRAKE, but not proportional and cannot adjust each aileron individually
Or use 2 Program Mixes, one for each aileron
    FLAP > AIL
    FLAP > AIL2

## Slide 41: Throttle to Elevator Mix
At high flap angles, airplane will pitch up strongly with increased power
Can be countered by mixing Throttle to Elevator
Can use separate mixes for different flap settings
Turn mixes on with switch used for flap setting
Using a curve mix can be helpful

## Slide 42: Throttle to Elevator - Spektrum
Landing Flaps
Mid Flaps

## Slide 43: Throttle to Elevator Futaba

## Slide 44: Flight Modes (Spektrum) Conditions (Futaba)
Flight Modes (Conditions) can remember individual TRIM states for various flight configurations controlled by one or two switches
Makes initial trimming flights much easier – just trim for each configuration
R/C sailplanes control camber across the whole wing
  Launch, cruise, penetration, thermal, spoilers, crow, flaps, etc.
RC airplanes
  Takeoff config, landing config, flap settings, gear position, speed brakes, crow, etc.

## Slide 45: Flight Modes - Spektrum

## Slide 46: Flight Mode Trim setup - Spektrum
Must change to F Mode for trim settings to be remembered in each Flight mode

## Slide 47: Flight Modes - Futaba
Available in Glider model type
Can be used for airplanes too
Highly flexible and capable Conditions can control any surface, landing gear, spoilers, trim, rates, expo, etc on one switch, or combination of switches.
Beyond the scope of tonight’s presentation!
Read the manual and check youtube videos of sailplane programming

## Slide 48: Throttle Cut on a Knob
On Spektrum, built-in Throttle Cut function forces you to use a switch to cut throttle for safety
BUT the switch can easily be bumped in flight or confused with another switch, shutting down the motor.
Knob > Throttle mix solves this

## Slide 49: Throttle Cut on a Knob - Spektrum
Knob is assigned to channel AX3 in
System Setup
/ Channel Assign
/ Channel Input Config

## Slide 50: Throttle Cut on a Knob Futaba
Switch G is a knob

## Slide 51: Ignition Kill Switch
AMA recommends for gasoline ignition engines in addition to throttle trim or throttle cut
Ignition kill device plug into a separate channel
Assigned to a knob or switch

## Slide 52: Ignition Kill - Spektrum
AX3 is the channel used for the ignition cut system in this model
AX3 is assigned to the knob
Knob used to turn ignition on prior to start
Can also use a mix to kill ignition quickly regardless of knob position. Mix 7 forces AX3 to zero by activating the spring-loaded Rtrim switch either direction

## Slide 53: Ignition Kill - Futaba
Use programmable mixes, mix knob, slider, or any switch to the ignition kill channel

## Slide 54: Throttle Curve
Used to make power feel more “linear”
That is, same amount of power for stick movement at both low and high throttle
Engine throttle responses are often not linear

## Slide 55: Throttle Curve - Spektrum

## Slide 56: Throttle Curve - Futaba

## Slide 57: Differential Thrust for Multi-Engine Planes
Enables better control of multi-engine seaplanes when on the water, especially if there is wind
  Assign throttle channel to Left engine
  Throttle > aux channel for Right engine throttle
  Rudder > Throttle (left Engine)
  Rudder > aux channel (right Engine)
If glow or gas, make sure rudder input while throttle is at idle won’t kill the engine
Use curve mix so that rudder only increases the thrust on one engine and does not reduce throttle on the other engine

## Slide 58: Differential Thrust - Spektrum

## Slide 59: Differential Thrust - Futaba
Same concept as for Spektrum, using programmable mixes

## Slide 60: VTOL Concept Using Free Mixes
Quad copter configuration in hover
Use Flight Modes and Flap function to tilt motors forward from hover, to transition, to cruise.
Flaps, wings, or other parts might tilt with the motors
Use mixes to create “copy” inputs of pitch, roll, and yaw to the quad controller, e.g. ELE > AX4, AIL > AX5, …
Flight Mode switch turns mixes off in forward flight to prevent quad controller from interfering with aerodynamic controls – quad controller then only controls thrust.

## Slide 61: Logical Switches (Futaba) Combo Mixing (Spektrum)
Mixes or other functions enabled by two switches
Function ON with switch 1 AND switch 2
  both must in desired position
Function ON with switch 1 OR switch 2
  either switch will activate
Can be switches, sticks, knobs, or sliders

## Slide 62: Why would you need a Logical Switch?
Example: Nose Gear steering rate
3 mixes of RUD > nose gear channel
    One for gear up (no steering, zero rate)
    One for takeoff (low rate, say 40%)
    One for taxiing (high rate, 100%)
Zero rate when Gear switch is up to center the nosewheel
Takeoff rate when gear is down AND throttle above some value
Taxi rate when gear down AND throttle below some value